BREAKAWAY HOLES ON CONSTRUCTION SIGNS

During this year’s Traffic Control Reviews, the issue arose as to whether “extra” holes are allowable in 6 inch by 6 inch wooden sign posts used during construction.  Traffic Control subcontractors are sometimes recycling the posts, and reusing them on subsequent projects.  This Construction Bulletin will clarify what is allowable regarding breakaway holes.

Subsection 630.3.4, #4 of the Construction Manual is hereby deleted and replaced with the following:

630.3.4, #4 Breakaway Bases.  Standard Specification subsection 630.02 states that construction traffic sign materials shall conform to the applicable portions of Section 614.  Standard Specification subsection 614.02, in the next-to-last paragraph, states that timber sign posts 6 inches by 6 inches shall be provided with two 2-inch diameter holes through the neutral axis at right angles to the roadway, one at 4 inches and one at 18 inches above the ground level.

Holes in addition to those described above are not allowed under any circumstances.  Additionally, holes in incorrect locations cannot be repaired using putty or any other substance.

Posts that do not meet these conditions should be rejected and replaced.

Please see CDOT Standard Plan S-614-5, sheet 1 of 2, for clarity.

If you have questions, please contact Randy Furst in Project Development at 303-757-9233.