PRE-ERECTION CONFERENCE AND ERECTION PLAN

This Construction Bulletin supersedes Construction bulletin 2004 -3, dated August 9, 2004.

CDOT Standard Specifications require an Erection Plan and a Pre-Erection Conference on projects with steel or concrete girders.  These requirements have been modified by two standard special provisions dated November 30, 2006:

- Revision of Section 509 – Erection of Steel Structures

- Revision of Section 618 – Erection of Pre-Cast Concrete Members

The specifications require that the Contractor submit an Erection Plan prepared by a Professional Engineer registered in the State of Colorado.  This plan shall be submitted for record purposes only.

A Pre-Erection Conference will be held at least one week prior to the beginning of erection.  The Contractor, the erection subcontractor, the Contractor’s Professional Engineer and the bridge designer shall attend the meeting.  The agenda for this conference has been revised.  A copy of the revised agenda for this conference is attached to this document.

During the erection process the Contractor’s PE shall be onsite to provide written approval of each stage of erection prior to allowing vehicles or pedestrians on or under the structure.  Changes to the erection plan shall be authorized by the Contractor’s PE. The Contractor shall also perform daily inspections of the girders until the deck is placed.

The Project Engineer will be familiar with the erection plan and will also monitor the erection process to ensure compliance with the erection plan.  The Project Engineer, or designated inspector, will also inspect the girders daily until such time as the deck is placed.  These inspections will be documented in the daily diary.

If you have questions, contact your Area Engineer in Project Development.

Here is the revised pre-erection conference agenda: