Revision to Stormwater Management Plan (SWMP)

This Construction Bulletin supersedes Construction Bulletin 2006-3.  This bulletin gives instructions on the implementation and interpretation of the revised Stormwater Management Plan (SWMP) plan sheet templates and the project special provision that are attached to this Bulletin and were issued on June 29, 2007.  Another change is the implementation of a SWMP Notebook that is to be maintained in the project field office at all times.

These actions were initiated by the Executive Stormwater Management Committee to comply with the new CDPS General Permit for Stormwater Discharges Associated with Construction Activity.  The new permit was issued by the Colorado Department of Public Health and Environment on May 31, 2007 and will become effective July 1, 2007.

The new project special provision, Revision of Sections 101, 107, and 208 – Water Quality Control contains much of the text that previously would have appeared on the SWMP plan sheets.

The SWMP Notebook shall contain:

  - SWMP Plan Sheets

  - SWMP site map and project plan title sheet

  - Copies of subsection 107.25 and sections 207, 208, 212, 213, and 216 of  the Standard Specifications, and all of the standard and project special provisions that modify them

  - M&S Standard Plan M-208-1

  - Details of BMPs used on the project not covered in Standard Plan M-208-1

  - Narratives related to BMPs used on the project not covered on the SWMP plans or site maps

  - Calendar for marking when the regular 14 day inspections take place and when the storm event inspections take place

  - All project permits, including, CDPS-SCP, SB 40, Dewatering, and all other permits applicable to the project.

  - List of all potential pollutants as described in subsection 107.25

  - Spill Prevention, Control and Countermeasure Plan

  - Form 1176 Inspection reports and RECAT reports

  - Form 105s relating to water quality

  - Description of inspection and maintenance methods implemented at the site to maintain all erosion and sediment control practices identified in the SWMP

The initial SWMP Notebook will be prepared by the designer and contain those items developed as a part of the design process and available at the time of advertisement.  The Contractor's Erosion Control Supervisor shall add the other items as they become available and update the notebook during construction. The SWMP notebook is the property of CDOT and shall remain with the project records at all times.

Revise all construction projects that have a Stormwater Construction Permit and meet the following criteria:

- They are under AD, Bid, or Award as of July 1, 2007, and

- They will not have a final acceptance letter issued by October 1, 2007.

On such projects make the following changes immediately:

- Designate and identify in the SWMP a SWMP Administrator (normally the ECS).

- Identify and record potential pollution sources as required by subsection 107.25 in the new special provision.

- Amend SWMP to include descriptions and installation specifications (design details) on how each BMP is being used.  Description includes a general description of the BMP and a site specific application.  Sample general descriptions can be found in the CDOT Erosion control and Stormwater Quality Guide.  Include BMPs for the following:

- Dedicated asphalt or concrete batch plants

- Vehicle tracking control

- Waste management and disposal (including concrete washout activities)

On such projects make the following changes by October 1, 2007:

- Void the original SWMP plan sheets and replace them with the June 29, 2007 issued SWMP plan sheets.

- Incorporate the new project special provision.

- Prepare the SWMP Notebook.  Include all contract documents and reports listed that are available up to this point.  Deliver the Notebook to the project.  Notify the Contractor that it is now his ECS's responsibility to keep the Notebook up to date.

Make these changes by Revision Under Ad or Change Order.  Contact Project Development Branch (Dennis Largent at 303-757-9595 or Karen Sullivan at 303-757-9502) if you need assistance with the Change Order.

SWMP Administrators (those conducting the 30 day inspections) on projects which are post construction, but still have open permits will need to incorporate these changes into the SWMP for these projects by October 1, 2007 as well.

Construction Bulletins can be found on the Design and Construction Project Support web page at:

http://www.dot.state.co.us/DesignSupport/

SWMP Template Sheets can be found on the Design and Construction Project Support web page at:

http://www.dot.state.co.us/DesignSupport/Typical%20CDOT%20Hwy%20Plan%20Sheets/Library%20Index.htm

The project special provision is a worksheet and can be found on the Design and Construction Project Support Web Page at:

http://www.dot.state.co.us/DesignSupport/Construction/2005SpecsBook/Work%20Sheets/2005ws.htm

If you have questions, please contact your Area Engineer in Project Development.

Attached are the SWMP project special provision:

Project Special Provision