Bridge Construction Reviews

This construction bulletin revises the CDOT Construction Manual to provide guidance on conducting final bridge construction reviews.

# Add Subsection 101.103.8.3 to the CDOT Construction Manual:

# 101.103.8.3 Bridge Construction Reviews

# Notify Staff Bridge upon construction completion of every structure that meets the federal definition of a major bridge.  A major bridge is any structure that carries vehicular traffic and is over twenty feet long, measured along the centerline of the roadway.  In addition to these structures, pedestrian and railroad structures over state highways will be included.  Staff Bridge shall conduct a final inspection for acceptance of all major structures before project final acceptance is granted.  Coordinate Staff Bridge final inspection with the completion of the structure so that any additional work that is required as a result of the inspection can be performed by the structure contractor without having to remobilize.

# Schedule the review by contacting the Staff Bridge PE II assigned to the Region.