# WATER QUALITY CONTROL UPDATE NO. 2

# On December 23, 2008 CDOT issued:

# Standard Special Provision Revision of Sections 101, 107, and 208 – Water Quality Control

# Construction Bulletin No. 2008-12 – Implementation of the Water Quality Control Consent Order

# The specification change and its implementation have generated questions and discussion both within CDOT and from Contractors.  Clarifications as needed will be provided by the Project Development Branch and Environmental Programs Branch to ensure statewide consistency in implementing and applying this special provision.  The purposes of this bulletin are to:

# Provide guidance on Project Job Showings for emphasis on Water Quality.

# Issue the Environmental Preconstruction Agenda.

# Project Job Showings

# With the added emphasis on Water Quality for all CDOT projects, the optimum time to begin addressing water quality and erosion control is at the job showings.  CDOT personnel shall review with all bidders at all job showings the project SWMP plans along with the Standard Special provision implementing the Water Quality requirements for the projects.   The Project Showing Form, Form No.1389, should be used to document the bidders’ questions and the responses from CDOT.

# Environmental Preconstruction Conference Agenda

# (Required for those projects with a Stormwater Permit)

# The agenda, which is attached, will be available in electronic format in the Appendix of the CDOT Construction Manual at the following link:

# http://www.dot.state.co.us/DesignSupport/ConstructionManual/Construction%20Manual%20Revisions%202004/Forms/Appendix%20A/Agenda%20Forms.htm

# The Environmental Preconstruction Conference meeting is a requirement of the CDOT specifications and Consent Order on all projects holding a Stormwater Construction Permit.  CDOT standard special provision, Revision of Sections 101, 107, and 208 – Water Quality Control, issued on December 23, 2008 requires under subsection 208.03 that:

# “Prior to construction, an on-site environmental preconstruction conference shall be held.  The conference shall be attended by the Engineer, the Superintendent, the Contractor’s ECS, subcontractors beginning work on the project that could adversely affect water quality, the Region Water Pollution Control Manager, other CDOT Region Environmental personnel, a CDOT hydraulics engineer as needed, and the CDOT Landscape Architect or CDOT personnel who prepared or reviewed the SWMP.  At this conference, the attendees shall discuss the stormwater management plan, CDPS-SCP, sensitive habitats on site, wetlands, and other vegetation to be protected.”

# The purpose of the conference is to ensure that all workers on site are aware and understand their role in implementing the erosion control/water quality requirements for the project. During each meeting, CDOT shall explain the requirements of the CDPHE Stormwater Permit (SCP), the site-specific SWMP, and all other environmental requirements for the site.  At the conclusion of each conference, CDOT shall require all attendees to sign a certification that they understand the terms and conditions of the Permit and the site’s associated SWMP.

# If a subcontractor begins work at the site after the environmental pre-construction conference has occurred, CDOT’s Project Engineer and the project superintendent shall hold a post conference briefing with all subcontractors not attending the original conference on the site’s SWMP and the Permit requirements before the subcontractor begins work at the site.  Attendees of the post conference briefing will then be required to sign a certification that they understand the terms and conditions of the Permit and the site’s associated SWMP.

The attached agenda will be handed out and used by the person conducting the Environmental Preconstruction Conference, and it will be left with the ECS to be placed in the SWMP notebook.  Here is the agenda and the certification signature sheet:

The Environmental Preconstruction Conference can occur as part of the regular preconstruction conference or as a separate meeting at a different date (e.g., at the initial BMP inspection) as agreed upon by the Project Engineer and Superintendent.

For the preconstruction conference to be the most effective, the SWMP notebook shall already be put together to the greatest extent possible.  The Engineer shall provide the following:

- The notebook including tabs

- Table of contents for maintaining the order of documentation within the notebook

- SWMP site map and project plan and title sheet

- Copies of subsection 107.25 and sections 207, 208, 212, 213, and 216 of the Standard Specifications, and the Standard and project special provisions that modify them

- Standard Plan M-208-1

- Calendar for marking when the 14 day inspections take place and when the storm event inspections take place

- All project environmental permits and associated applications, including, CDPS-SCP, Senate Bill 40, USACE 404 permit (if applicable), and all other permits applicable to the project, including any CDPS-SCP obtained by the Contractor.

If possible, the Contractor should have submittals that are required prior to construction commencing prepared for the meeting including but not limited to:

- Copy of Project Schedule as required under subsection 208.02(b)

- Erosion Control Supervisor Card

- Potential pollutants list - 107.25(b)5

- Spill prevention, control and countermeasure plan - 208.051

- Description of inspection and maintenance methods implemented at the site to maintain all erosion and sediment control practices identified in the SWMP.  (Including who is responsible for the maintenance of all erosion control measures, how the ECS can make available labor, material and equipment to maintain suitable erosion and sediment control features, and how and when BMPs are inspected and action items are dispatched to crew for repair or maintenance.)