Water Quality Update No. 3:

FAQ Water Quality Webpage, Daily Inspections, & Local Agency Projects

# On December 23, 2008 CDOT issued:

# Standard Special Provision, Revision of Sections 101, 107, and 208 – Water Quality Control

# Construction Bulletin No. 2008-12 – Implementation of the Water Quality Control Consent Order

# The specification change and its implementation have generated questions and discussion both within CDOT and from Contractors.  Clarifications as needed will be provided by the Project Development Branch and Environmental Programs Branch to ensure statewide consistency in implementing and applying this special provision.  This bulletin provides clarification of Daily Inspections and the application of the Consent Order to Local Agency projects.  Also, CDOT has included an addition to its webpage for Frequently Asked Questions for Water Quality Control.

FAQ Water Quality Webpage

In response to both the number and variety of questions concerning the implementation of the Revision to the Water Quality Control specification, CDOT has created a webpage with questions from Contractors and CDOT field personnel and their associated responses.  See the major heading, “Water Quality Control” on the Design and Construction Project Support web page at the link below for access to this site:

http://www.dot.state.co.us/DesignSupport/

Daily Inspections

The requirements for “daily inspections” are included in Subsection  208.03(c)17 of the Revision of Sections 101, 107, & 208 - Water Quality Control, issued on December 23, 2008, which reads:

The ECS or the Superintendent shall conduct an inspection on each day in which active construction has occurred.  At this inspection the entire site shall be reviewed to determine whether construction is being conducted in accordance with the project’s site-specific SWMP and the CDPS-SCP.  The ECS or Superintendent shall observe, record, and determine the effectiveness of all BMP’s.  Inspections shall be recorded on the Daily Stormwater Log and kept in the project SWMP notebook.

Daily inspections are required for all installed BMP’s on the project.  As part of the inspection, the entire site shall be reviewed to ensure that the installed BMP’s are performing properly and no other water quality issues have arisen.

Local Agency Projects

Clarification has been received from CDPHE regarding how the Consent Order will affect Local Agency (LA)  projects. All existing Local Agency projects on which an inter-governmental agreement (IGA) was completed by January 1, 2009 are exempt from the provisions of the Compliance Order on Consent.  If this has not occurred then the LA would need to comply with the Consent Order language.

For those Local Agency projects that are currently exempt, use the Revision of Sections 101, 107 & 208 Water Quality Control specification issued July 12, 2007.  The specification is available on the CDOT web site at:  http://www.dot.state.co.us/DesignSupport/Construction/2005SpecsBook/Work%20Sheets/101wqc%20corrected%207-12-07.doc .

Local Agency projects that are not exempt and to which the Consent Order applies as shown in the table below shall include the appropriate one of the following special provisions:

- Revision of Sections 101, 107 & 208 Water Quality Control specification released on December 23, 2008 for those projects requiring a CDPS-SCP (more than 1 acre of disturbance)

- Revision of Sections 101, 107 & 208 Water Quality Control specification released on January 21, 2009 for those projects not requiring a CDPS-SCP (less than 1 acre of disturbance)

| Project Type | Right of Way Owner | Permit Holder | Consent Order Applies? |
| --- | --- | --- | --- |
| LACA Project with CDOT administering Federal/State Funds | 100% Other | LA/Municipality | No |
|  | X% other, X% CDOT | LA/Municipality | Yes, for the portion in CDOT ROW |
|  | 100% CDOT | LA/Municipality or CDOT | Yes, for entire project |
| Access/Utility Permits | All | LA/Municipality/Utility | No |

If you have questions, contact your Area Engineer in Project Development.