Overweight Hauling Vehicles

Recent changes in Colorado law have resulted in the potential for hauling vehicles with overweight permits to deliver materials to non-interstate construction projects.  CDOT has issued a revision to subsection 109.01of the Standard Specifications that requires the Contractor to provide information on such vehicles that will be used on the project.  This revision has been incorporated into the standard special provision, Revision of Section 109 – Measurement of Quantities.  This construction bulletin revises the guidance given in Section 121.2.1 of the Construction Manual regarding collecting that information.

Revision of Section 109

Revisions to the Construction Manual

In Section 121.2.1 replace item 4. b. with the following:

  - Certifications. Attach one copy of scale and weigher certifications and vehicle identification sheets with the applicable pay item documentation that is submitted to the Region. The vehicle identification sheets furnished by the Contractor must contain the following information:

- Identification mark,

- vehicle length,

- tare weight,

- number of axles,

- the distance between extreme axles

- information relative to determining legal weight, including the permit No. and permitted weight of each vehicle for which the State has issued an overweight permit

Obtain new copies of this information whenever there is a change.

Add the following to the information on vehicle sizes and weight limits on pages D-3 through D-7 of Appendix D:

CDOT Non-Interstate Overweight Divisible Permits

Fact Sheet

Non-Interstate Quad Axle Overweight Divisible Permits

Effective October, 2008

- Overweight permits only (no oversize/over dimension)

- Non-interstate highways only

- Vehicle must be configured with a quad axle grouping

- Cannot exceed 110,000 lbs. gross vehicle weight

- Must comply with maximums on CDOT Bridge Weight Limit Map

- Single trip permit available. Fee: $30 + $10 per axle

- Annual permit available. Fee: $500

- Annual Fleet Permit available. Fee: $2,000 + $35 per permitted vehicle

- Substantial fines may be assessed for violations

Non-Interstate Tandem/Triple Axle Overweight Divisible Permits

Effective January 1, 2010

- Overweight permits only (no oversize/over dimension)

- Non-interstate highways only

- Applies to tractor/trailer combination vehicles only

- Must have either tandem or triple axle grouping on trailer

- Cannot exceed 97,000 lbs. gross vehicle weight

- Must comply with maximums on CDOT Bridge Weight Limit Map

- Single trip permit available. Fee: $15 +$10 per axle, plus a surcharge equal to the total amount of the permit

- Six-month permit available. Fee: $250

- Annual permit available: Fee: $500

- Substantial fines may be assessed for violations

To view Legislation click on the respective link:

- Quad Axle Non-Interstate Overweight Divisible Permits – HB 08-1257

- Tandem/Triple Axle Overweight Divisible Permits – HB 09-1318

Fact sheet compiled September 16, 2009