PROJECT SAFETY PLANNING SPECIFICATION REQUIREMENTS

This construction bulletin is intended to assist with the implementation and interpretation of the Revision of Section 107 - Project Safety Planning standard special provision dated July 30, 2009, which is available at:

http://www.dot.state.co.us/DesignSupport/Construction/2005SpecsBook/2005SSP/2005_SSP_Index.htm

Delete section 107.6 of the CDOT Construction Manual and replace it with the following:

107.6 SANITARY, HEALTH, AND SAFETY PROVISIONS

107.6.1 CDOT Safety Manual

The CDOT Safety Manual contains information regarding personal safety practices and protective equipment to be used for specific work conditions.

107.6.2 Safety Equipment

Required personal protective equipment (including but not limited to hard hats, vests, eye protection, and foot protection) will be made available, and will be properly used by, all CDOT personnel and consultants pursuant to Procedural Directive 80.1 which is available at: http://internal/PolicyGovernRelations/tracking/PDs%20for%20Web/0080-1%20PPE%20Use%20_2_%202%2024%2006.pdf .

Consultants working on CDOT projects must wear the same personal protective equipment as CDOT personnel.  Appropriate safety equipment will be utilized as required by the specific work conditions and current policy.

107.6.3 Responsibilities and Authority

The Contractor is responsible for complying with all safety, health and sanitation laws, rules, regulations, and guidelines, including but not limited to the Project Safety Management Plan (Plan) described in the specification, the Occupational Safety and Health Act (OSHA), 29 CFR 1910, 29 CFR 1926, 23 CFR 634,  the Mine Safety and Health Administration (MSHA), Title 30 CFR, “Colorado Work Zone Best Practices Safety Guide”, CFR 49, national consensus standards, and the Drug Free Workplace Act, and for ensuring the safety and convenience of all representatives and employees of the Contractor and all subcontractors, suppliers, Department personnel and consultants, visitors, and the public throughout the project site.

The specifications require the Contractor to prepare a project-specific Plan.  The Contractor must certify that:

- The Plan complies with applicable safety, health, and sanitation laws, rules, regulations, and guidelines.

- All operations and work practices of the Contractor comply with it.

- All subcontractors, suppliers, and Department personnel and consultants will comply with it.

The Contractor is to submit a copy of this Plan to the Engineer before starting work, and is to keep it updated.  The Engineer should be familiar with the specification and the Plan.  The Engineer should review the Plan for general adequacy and compliance with the specification, and notify the Contractor in writing that the plan has been received and addresses items 1 thru 12 in the special provision.   The Engineer should request assistance from the Region Safety Officer.

An example project safety management plan has been posted on the 2005 Construction Specifications page of CDOT's web site.   Notice that this is only an example project safety management plan.  It may be used only as a guide in preparing an actual project safety management plan.  The safety management plan for a particular project must address the specific construction activities on that project. Those activities will likely be different from the ones in the posted example project safety management plan.    The URL for the CDOT web page on which the example plan may be found is:

http://www.dot.state.co.us/DesignSupport/Construction/2005SpecsBook/2005index.htm

Among other things, the specification requires at a minimum that all personnel on the project site are to wear hard hats, high visibility apparel and appropriate, sturdy footwear at all times when outside of their vehicles and within CDOT ROW.  Consider the following additional guidelines:

- CDOT Responsibility and Authority. The Department will not permit any employee to work in or around unsanitary or unsafe conditions. All CDOT and Consultant personnel on the project should monitor Contractor and subcontractor activities for obvious or suspected noncompliance with the Plan, and safety, health and sanitation laws, rules, regulations, and guidelines.  Any concerns should be raised immediately and followed up in writing with the Contractor’s competent person for that activity, the Superintendent, or the Contractor’s Project Safety Manager.  Due to training and liability constraints, the Department does not have the authority to accept a specific condition as being in compliance with OSHA requirements.  Furthermore, it is not the intent of the specification for CDOT or Consultant personnel to function as OSHA enforcement or OSHA inspectors.  The Contractor is responsible for compliance with its Plan.

- Noncompliance. The Project Engineer will immediately notify the Contractor in writing of apparent noncompliance with the Plan, or other laws, rules and regulations.  The specification requires the Contractor to respond in writing to safety issues raised by the Engineer.  The Engineer should contact the Region Safety Officer or the Safety Officer in the Maintenance and Operations Branch at (303) 273-1849 for assistance.

3. 	Imminent Danger. Imminent danger is any situation or condition on the project that could, in the opinion of the Project Engineer, result in serious injury or death. It should be noted that subsection 105.01 of the Standard Specifications already requires the Engineer to immediately suspend all or part of the work when the Contractor fails to correct conditions unsafe for the workers or the general public.  Additionally, the Project Safety Planning special provision now allows the Engineer to immediately enact a “safety stand-down” in the case of an accident (including property damage), or catastrophe (where three or more people go to the hospital in one incident), or other situation presenting an imminent danger to life or health, such as a “near miss”, violation of the Plan, or presence of a hazardous situation.  The safety stand-down is mandatory in the case of a work zone fatality directly related to the Contractor’s or any subcontractor’s operations.  The Engineer will need to apply judgment in non-fatal situations, in cases of vehicular fatality not caused by a work zone incident, and for minor infractions.  The Contractor is required to provide properly certified documentation specifying the corrective measures that it has taken to prevent recurrence, before the Contractor may resume operations.  Contact the Region Safety Officer or the Safety Officer in the Maintenance and Operations Branch for assistance with questionable situations and for review of the Contractor’s corrective measures.

The Engineer should withhold progress payments, suspend the project, or both for failure to submit an acceptable Plan or update it, for failure to respond in writing to safety issues that are raised by the Engineer, or for failure to submit documentation of safety inspections.

If you have questions, please contact one of the Area Engineers in Project Development.