Construction Traffic Control

Standard Special Provision – Revision of Section 630 – Construction Zone Traffic Control dated November 30, 2000.

This bulletin was released to explain the significant changes in this specification and to help ensure that all projects are administered consistently.

Subsection 630.14 of this Standard Special Provision contains a list of the minimum information to be included in the Traffic Control Supervisor’s diary, which must be submitted to the Project Engineer.

This section also clarifies the off-hours response requirements.  The TCS or another person must respond to the jobsite within 45 minutes.  If the person who responds is not a certified work site supervisor, someone who is must respond to the job site within two hours from the initial call out.

Subsection 630.14 of this Standard Special Provision contains the following provisions:

“The quantity to be measured for Traffic Control Management will be the number of authorized 24-hour days of active TCM performed by the TCS or another representative certified as a worksite traffic supervisor.  Payment will be made for one day of Traffic Control Management regardless of the number of TCSs required to adequately control the work”

The Traffic Control Management pay item replaces the old Traffic Control Supervisor pay item.  This was done to help distinguish between the pay item and the person.  The pay item includes payment for a 24-hour day of traffic control management, regardless of the number of traffic control supervisors required to conduct the work.

Example:  A contractor may decide to work both a day shift and a night shift on a project.  If traffic control is needed during both shifts, a TCS will need to be provided for both shifts.  For night shifts that begin prior to midnight and end after midnight, the TCM is charged on the day the shift ends.  In our example, if the contractor worked a Sunday night shift and a day shift on Monday, they would be paid one day of TCM on Monday.  If the Sunday shift ended prior to midnight, the contractor would be paid one day of TCM on Sunday, and one day of TCM on Monday.

“The quantity to be measured for flagging will be the total number of actual flagging hours that are used as authorized in accordance with an approved MHT.  Payment will not be made for time spent by flaggers to set up and take down construction traffic control devices”.

This revised language is intended to clarify what will be paid as flagging hours.  Only actual hours of flagging performed are paid for.  Actual flagging is when a flagger is performing flagging duties as authorized in a MHT.  Set up of lane closures, maintenance of devices, extra flaggers to provide breaks, and show up time are not actual flagging and are not paid for.

Example 1:  The TCS utilizes flaggers to assist in setting up the flagging stations or lane closures.  There is no flagging payment for this work.  Payment is included in the devices.

Example 2:  Six flaggers are on the road actively flagging from 8:00am to 10:00am.  Two flaggers are on the road actively flagging from 10:00am to 12:00pm and the other four flaggers are cleaning devices.  Six flaggers are on the road actively flagging from 12:00pm to 4:00pm.  There would be no compensation for the four flaggers not utilized for flagging between the hours of 10:00am and 12:00pm.

Example 3:  Weather conditions shut the project down prior to the beginning of operations but after all of the flaggers have assembled at the site.  As there is no compensation for “show-up” time allowed, there would be no payment for flagging.

Example 4:  The TCS utilizes a break flagger to relieve 5 other flaggers for lunch breaks. Since there are only 5 authorized flagging locations, payment would be for the number of hours that the 5 flagging locations were manned.  The break flagger is only utilized to keep the flagging stations manned full time, and would not be paid as an extra flagger.