Curb Ramps with Landings and Detectable Warnings

Revised Guidelines have been adopted by The Access Board under the American Disabilities Act (ADA) defining traversable slope requirements and prescribing the use of a defined pattern of truncated domes as detectable warnings at street crossings.  The regulations issued by DOJ and USDOT state projects must include accessibility standards for newly constructed and altered facilities covered by Title II.  The standards must be consistent with the guidelines issued by the Access Board.

CDOT is issuing new Standard Plans and Standard Special Provisions to follow the Access Board requirements.  New Standard Plan M-608-1, Curb Ramps (4 sheets), and associated Project Special Provision, Revision to Section 608 – Curb Ramps (Detectable Warnings), will be used for construction projects advertised on or after November 26, 2003, for installing new and replacing existing curb ramps.   Earlier use is permissible.

The DOJ has determined that on all projects, curb ramps shall comply with the new ADA guidelines, regardless of ROW ownership or jurisdiction.  This mandate also applies to resurfacing projects.  Application requirements for specific types of projects are detailed in the attached document “ADA Accessibility Requirements” with the transmittal from Tom Norton, CDOT Executive Director.

Alternate materials and other construction techniques for truncated dome detectable warnings may be used with concurrence of the Standards & Specifications Unit.  Requests for information are out to other suppliers and manufacturers of pavers and other detectable warning systems.  The attached Detectable Warnings Material Suppliers List will be updated and redistributed as it is received.  Don't hesitate to contact CDOT Standards & Specifications with any comments or questions.

The new Standard Plans and Project Special Provision can also be found on the Design and Construction Project Support web page at: http://www.dot.state.co.us/DesignSupport/

For paper copies of project details and project special provisions, or should you have any questions or concerns on the application and use of the revised Standard Plan or project special provision, please call:  CDOT Standards & Specifications at (303)757-9474.