Overlay Exemption from MS4 requirements

Clarification of the requirements of CDOT’s MS4 (Municipal Separate Storm Sewer System) permit as it relates to Overlay projects has been obtained.

Effective immediately, overlay projects meeting the following criteria are considered to be maintenance activities and are exempt from the permanent BMP (Best Management Practices) requirements of the MS4 permit.

- Does not change the existing template of the roadway including shoulders.

- Does not expose sub-base or sub-grade.

- Does not widen the roadway.

- Does not pave previously unpaved shoulders.

- Surface treatment does not exceed 6” total depth.

- Other project work beyond the shoulders does not disturb one acre or more.

Attached below are: the memo to the Chief Engineer, the letter from the Chief Engineer to the Colorado Department of Public Health and Environment, (CDPHE) Water Quality Control Division (WQCD), the response from CDPHE – WQCD, the CDPS permit, and the permit rationale.

Design Bulletins can be found on the Design and Construction Project Support web page at:

http://www.dot.state.co.us/DesignSupport/

If you have any questions, please call David Wieder at 303-757-9233.