Project Signs for Funding Advancements for Surface

Transportation and Economic Recovery (FASTER) Projects

This design bulletin provides guidance on the design and placement of mandatory signs to be installed on projects that are funded with FASTER funds.

CDOT Management has decided that all projects funded with FASTER money (both bridges and safety) shall have special signs identifying them as FASTER projects.  The signs are to be erected at each major approach to the project.  There will normally be a minimum of two of these signs on the project.  Since there may be special circumstances, the project manager should consult the Region Traffic Engineer on the number and locations of signs. The sign layout consists of two panels, a W21-1a “Workers Sign” sign mounted on a special FASTER sign.  Attached is the electronic file of the sign layout.

Signs shall be mounted on 6 X 6 timber posts for a temporary installation in accordance with the applicable S-Standards.  These signs will be paid for using bid item 630-80344, Construction Traffic Sign (Special).

The sign layout can be accessed via the HQ Safety and Traffic Engineering Branch website under the link to the CDOT Sign Library webpage at http://www.coloradodot.info/library/traffic/traffic-manuals-guidelines/fed-state-co-traffic-manuals/cdot-sign-library.html

If you have questions, please contact your Area Engineer in Project Development.