627tpmwhma

08-01-05

REVISION OF SECTION 627

TEMPORARY PAVEMENT MARKINGS

ON WARRANTED HOT MIX ASPHALT

Section 627 of the Standard Specifications is hereby revised for this project as follows:

Subsection 627.03, first paragraph, shall include the following:

When paving is complete and the specified permanent pavement markings cannot be installed in compliance with the specifications, the Contractor shall install and maintain, at its own expense, temporary full compliance pavement markings conforming to subsection 627.04 or 627.08.  The temporary markings shall be maintained until the specified permanent markings have been installed in compliance with the specifications and accepted.  If tape is used for the temporary pavement marking it shall be removed prior to final acceptance.