Sample project special: 604msdm

08-01-05

REVISION OF SECTION 604

MANHOLE SPECIAL (DEEP MANHOLE)

Section 604 of the Standard Specifications is hereby revised for this project to include the following:

Subsection 604.01 shall include the following:

This work includes the construction of one deep manhole at the location and to the dimensions shown on the plans or as established.

Subsection 604.06 shall include the following:

Manhole Special will be measured by the complete unit in place and accepted, including manhole platform and precast concrete slab.

Subsection 604.07 shall include the following:

Payment will be made under:

Pay Item									Pay Unit

Manhole Special (35 Foot)					Each

Deep Manhole ("H" greater than 20 feet) will be paid for as Manhole Special.