Sample project special: 617jtmp

08-01-05

REVISION OF SECTION 617

JOINT TREATMENT FOR METAL PIPE

Section 617 of the Standard Specifications is hereby revised for this project as follows:

Subsection 617.02 shall include the following:

If metal pipe is used, special joint treatment shall be provided to prevent exfiltration and infiltration.  The special treatment shall consist of neoprene gaskets or gaskets conforming to AASHTO M 198, Types A or B, except that parts 5, 6, and 8 shall not apply.  Coupling bands and gasket material shall be applied in accordance with the pipe manufacturer's recommendations.  Dimpled bands will not be acceptable.  Other types of joint sealing treatment may be used if approved by the Engineer.

Subsection 617.05 shall include the following:

Joint treatment of metal pipe will not be paid for separately, but shall be included in the work.