Sample project special: 304abcs

08-01-05

REVISION OF SECTION 304

AGGREGATE BASE COURSE (SPECIAL) AND

PLACE AGGREGATE BASE COURSE

Section 304 of the Standard Specifications is hereby revised for this project as follows:

Subsection 304.01 shall include the following:

Place Aggregate Base Course consists of hauling to the site and placing one or more courses of aggregate on a prepared surface in conformity with the lines, grades, and typical sections shown on the plans or established.

Subsection 304.02 shall include the following:

The material shown on the plans as Aggregate Base Course (Special) is available from the ________________ source listed and at the price shown elsewhere in these Project Special Provisions under Available Source of Materials.

The material shown on the plans as Place Aggregate Base Course will be furnished to the Contractor by _____________ at no charge and is available at the location listed elsewhere in these Project Special Provisions under Available Source of Materials.

Should the Contractor elect to supply any or all of the Aggregate Base Course from a Contractor source, then this material shall meet the requirements of subsection 703.03 as follows:

Aggregate Base Course (Special) shall meet the gradation requirements for Aggregate Base Course (Class 6).

Place Aggregate Base Course  shall meet the gradation requirements for Aggregate Base Course (Class 3).

Subsection 304.07 shall include the following:

Aggregate Base Course (Special) and Place Aggregate Base Course will be measured by the cubic yard in place.

Subsection 304.08 shall include the following:

Payment will be made under:

Pay Item							Pay Unit

Aggregate Base Course (Special)		Cubic Yard

Place Aggregate Base Course			Cubic Yard