Sample Project Special Provision: 412tbi

7/24/2006

REVISION OF SECTION 412

TIE BAR INSPECTION

Section 412 of the Standard Specifications is hereby revised for this project as follows:

Subsection 412.13(b) 1 shall include the following:

If tie bars are inserted into plastic concrete with a tie bar insertion machine, tie bar location and concrete consolidation shall be subject to the following additional requirements:

Each 2500 linear feet of longitudinal weakened plane joint resulting from the procedure shall have one random location cored where the core intercepts an inserted tie bar.  The core shall be six-inch diameter taken in the presence of the Engineer.

If non-consolidated concrete is evident above the inserted tie bar, the Contractor shall cease paving operations and submit a corrective action plan in writing for approval.  Correction of the joint and further paving shall take place only after written approval of the corrective action plan has been provided by the Engineer. Additional coring may be required, as directed by the Engineer.  Coring operations, including patching, shall be at the Contractor’s expense.

Further failure to consolidate the concrete over the tie-bars will be justification to preclude the use of automatic tie-bar insertion for the remainder of the project.