#### January 17, 2008

## Revision of Section 105

### Conformity TO THE CONTRACT

##### NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions issued unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on projects having HMA.

January 17, 2008

REVISION OF SECTION 105

CONFORMITY TO THE CONTRACT

Section 105 of the Standard Specifications is hereby revised for this project as follows:

Subsection 105.03 shall include the following, after the first paragraph:

All Hot Mix Asphalt (HMA) materials or work will be evaluated for conformity to the Contract in accordance with subsection 105.05 except HMA that is used for patching and temporary pavement.

In subsection 105.03 (c), delete the Table of Price Reduction Factors and replace with the following:

TABLE OF PRICE REDUCTION FACTORS

| Element | Factor “F” |
| --- | --- |
| 100 percent size sieve | 1 |
| 12.5 mm (½”) sieve and larger | 1 |
| 150 μm (No. 100) sieve to 9.5 mm (3/8”) sieve inclusive (except 100 percent size sieve) | 3 |
| 75 μm (No. 200) sieve | 6 |
| 75μm (No. 200) sieve (cover coat material) | 25 |
| Liquid Limit | 3 |
| Plasticity Index | 10 |
| Asphalt penetration | 1 |
| Asphalt residue | 3 |
| Portland Cement Concrete Pavement Fine Aggregate Sand Equivalent | 0.3 |
| Hydrated Lime Gradation | 0.3 |
| Toughness, inch-pounds, minimum | 0.8 |
| Tenacity, inch-pounds, minimum | 0.8 |
| Elastic Recovery, 25 °C, percent minimum | 1.25 |
| Ductility, 4 °C (5cm/min) cm, minimum | 1.25 |

In subsection 105.03 (c), delete the seventh paragraph, including the table of the multiplier for price reductions, and replace with the following:

If the P for aggregate gradation for Items 206, 304, or the gradation of hydrated lime for item 403 is 3 or greater the reduction will apply to the contract price multiplied by the Multipliers (M) listed in the following table:

Multiplier for Price Reductions for Miscellaneous Items

| Item Number-Name | Element | Multiplier (M) |
| --- | --- | --- |
| 206- Structural Backfill | Gradation | 0.60 |
| 304-Aggregate Base Course | Gradation | 0.60 |
| 403-Hot Mix Asphalt* | Hydrated Lime Gradation | 0.60 |

* The P value for hydrated lime shall be applied to the price of the HMA item when asphalt cement is not paid for separately. Lime gradation P values will not be combined with Pay Factors for other elements.