March 22, 2010

REVISION OF SECTION 630

SMALL SIGN SUPPORT (TEMPORARY)

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in projects having construction signing.

March 22, 2010

REVISION OF SECTION 630

SMALL SIGN SUPPORT (TEMPORARY)

Section 630 of the Standard Specifications is hereby revised for this project as follows:

Subsection 630.01 shall include the following:

This work includes the installation of perforated square metal tubing or U-channel as temporary sign supports at locations shown on the plans.

Subsection 630.02 shall include the following:

Temporary sign support assembly shall be either perforated square metal tubing inserted into a larger base post or slip base or perforated metal u-channel with a slip base. The temporary sign support assembly shall conform to NCHRP and AASHTO requirements regarding temporary sign supports during construction.

If U-Channel posts with a slip base are selected, they shall only be used in multi-post applications, as shown in Standard Plan S-630-4.

Subsection 630.12 shall include the following:

Perforated square metal tubing or u-channel shall be installed for temporary sign supports according to the manufacturer’s recommendations and as shown on the Plans.

The Contractor shall be responsible for all maintenance of the signs and posts. If a sign or post is damaged during construction, the contractor shall be responsible for replacing and maintaining the sign and posts at no additional cost to the Project.