February 25, 2010

REVISION OF SECTION 630

TRAFFIC CONTROL SUPERVISOR

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in all projects having traffic control.

February 25, 2010

REVISION OF SECTION 630

TRAFFIC CONTROL SUPERVISOR

Section 630 of Standard Specifications is hereby revised for this project as follows:

In subsection 630.10, delete the third paragraph and replace with the following:

A certified worksite traffic supervisor shall be responsible for Traffic Control Management (TCM) on a 24-hour-per-day basis.  The TCS shall be on the work site at all times when Traffic Control Management (TCM) is performed and shall be on call at all times.  Upon request of the Engineer, the TCS may be required to be on the project site at times other than normal working hours.   During non-work periods, the TCS shall respond to the job site within 45 minutes. The TCS may appoint a qualified representative to serve as the TCS for periods of time as approved by the Engineer.  The qualified representative shall be certified as a TCS, and shall assume all duties and responsibilities of the TCS. The Contractor shall maintain a 24-hour telephone number at which the TCS can be contacted. The TCS shall not act as a flagger except in an emergency or in relief for short periods of no more than 15 minutes over a 60 minute period.