### March 11, 2004

# REVISION OF SECTIONS 107 AND 412

CONCRETE WASTEWATER CONTAINMENT

## NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions regarding its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies that use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on projects having any type of concrete construction.

March 11, 2004

REVISION OF SECTIONS 107 AND 412

CONCRETE WASTEWATER CONTAINMENT

Sections 107 and 412 of the Standard Specifications are hereby revised for this project as follows:

Delete subsection 107.25(a) 3 and replace with the following:

3. State Waters.  Based on 25-8-103 (19) CRS, state waters are defined to be any and all surface and subsurface waters which are contained in or flow through the state, including, streams, rivers, lakes, drainage ditches, storm drains, ground water, and wetlands, but not including waters in sewage systems, waters in treatment works or disposal systems, waters in potable water distribution systems, and all water withdrawn for use until use and treatment have been completed.

Subsection 107.25(b)11 shall include the following:

Removal of concrete waste and washout water from mixer trucks, concrete finishing tools, concrete saw and all concrete material removed in the course of construction operations or cleaning shall be performed in a manner that prevents waste material from entering state waters.  A minimum of 10 days prior to the start of concrete operations, the Contractor shall submit in writing a method for containing concrete wastewater to the Engineer for approval.

Subsection 412.07(c) shall include the following:

Wastewater generated from concrete saw operations shall be contained and disposed of in accordance with subsection 107.25.

Subsection 412.12 shall include the following:

Wastewater generated from concrete finishing operations shall be contained and disposed of in accordance with subsections 107.25.