August 9, 2004

REVISION OF SECTION 509

ERECTION OF STRUCTURES

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on projects having steel structures and structural steel members.

August 09, 2004

REVISION OF SECTION 509

ERECTION OF STRUCTURES

Section 509 of the Standard Specifications is hereby revised for this project as follows:

Subsection 509.27 shall include the following:

Structural steel members shall be erected in a manner that will provide safety to the Contractor’s forces, inspectors and the traveling public. Structural steel members shall be erected in a manner to prevent damage to all elements of the structure. The primary members such as beams and girders shall be temporarily anchored and braced as they are erected to preclude detrimental movement in any direction, and to prevent overturning and buckling. Struts, bracing, tie cables, and other devices used for temporary restraint shall be designed to resist all loads imposed during each stage of construction until completion of the deck concrete.

At least four weeks prior to erection, the Contractor shall approve, sign and submit a proposed plan of erection to the Engineer for record purposes only. The Erection Plan shall be approved by, and contain the seal and signature of, the Contractor’s Professional Engineer registered in the State of Colorado. The Erection Plan will not be approved by the Engineer.  If falsework drawings are required, they shall be submitted in accordance with subsection 601.11.

The Erection Plan and procedure shall provide complete details of the erection process including but not limited to:

- Temporary falsework support, bracing, guys, deadmen, connection details and attachments to other structure components or objects;

- Procedure and sequence of operation including a detailed schedule that shall comply with the working hour limitations;

- Crane(s) make and model, weight, geometry, lift capacity, outrigger size and reactions;

- Girder weights, lift points, lifting devices, spreaders, and angle of lifting cables.

- Assumed loads and girder stresses during progressive stages of lifting and erection to substantiate the structural integrity and stability of the girders prior to completion of the entire structure;

- Girder launcher or trolley details and capacity (if intended for use); and

- Locations of cranes, trucks delivering girders, and the location of cranes and outriggers relative to other structures, including retaining walls, wing walls and utilities.

- Material properties and specifications for temporary works.

- Drawings, notes, catalog data showing the manufacturer’s recommendations or performance tests, and calculations clearly showing the above listed details, assumptions, and dimensions.

A Pre-Erection Conference will be held at least two weeks prior to the beginning of erection.  The Contractor and the Contractor’s Professional Engineer shall attend the meeting.

The Contractor’s Professional Engineer shall inspect and provide written approval of each phase of the installation prior to the allowing vehicles or pedestrians on or below the structure.  The Contractor’s Professional Engineer shall approve all changes to the Erection Plan.  The Contractor shall submit all changes to the Erection Plan to the Engineer for record purposes only. The Contractor shall demonstrate his knowledge and familiarity with the location of the piece marks and the piece mark convention used by the girder fabricator at the Pre-Erection Conference. This is required to assure the structural components are assembled in accordance with the reviewed shop drawings.

The Contractor shall perform daily inspections of the erected girders until completion of the deck concrete. The Contractor shall provide the Engineer with written documentation of these inspections within 24 hours.

All temporary struts, bracing, tie cables, other devices and extra material required shall be removed upon completion of the structure.

Subsection 509.33 shall include the following:

All costs associated with implementing the Erection Plan will not be paid for separately but shall be included in the work.