August 26, 2004

REVISION OF SECTION 630

NCHRP 350 REQUIREMENTS

###### NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions issued by the Project Development Branch unless such use is first approved by the Specification Unit of Project Development.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

# Use this standard special provision on all projects.

August 26, 2004

REVISION OF SECTION 630

NCHRP 350 REQUIREMENTS

Section 630 of the Standard Specifications is hereby revised for this project as follows:

In subsection 630.01 delete the 2nd sentence:

Subsection 630.08 shall include the following:

Work zone devices designated by FHWA as category I, including but not limited to single-piece drums, tubes, cones and delineators shall meet NCHRP 350 crash test requirements.  The Contractor shall obtain and present to the Engineer the manufacturer’s written NCHRP 350 certification for each type of category I device before it is first used on the project.

Work zone devices designated by FHWA as category II, including but not limited to barricades, vertical panels with light, drums or cones with light, portable sign supports, intrusion detectors and type III barricades shall meet NCHRP 350 crash test requirements. However, the Contractor may use category II devices originally purchased prior to October 1, 2000 in accordance with Table 630-2. The Contractor shall obtain and present to the Engineer the manufacturer’s written NCHRP 350 certification for each type of category II device or shall certify that the category II device was originally purchased prior to October 1, 2000 before it is first used on the project.

Work zone devices designated by FHWA as category III, including but not limited to concrete barriers, fixed sign supports, crash cushions, and other work zone devices not meeting the definitions of Category I or II shall meet NCHRP 350 crash test requirements.  However, the Contractor may use category III devices originally purchased prior to October 1, 2002 in accordance with Table 630-2.  The Contractor shall obtain and present to the Engineer the manufacturer’s written NCHRP 350 certification for each type of category III device or shall certify that the category III device was originally purchased prior to October 1, 2002 before it is first used on the project.

Work zone devices that do not meet NCHRP 350 requirements shall not be used after the phase out date.

#### Table 630-2

##### Phased Implementation of Work Zone Devices

| WORK ZONE DEVICES | COMPLIANCE DATE | PHASE OUT DATE |
| --- | --- | --- |
| Category I | October 1, 1998 for new installations. | N/A |
| Category II | October 1, 2000 for new installations. Existing devices may be used until service life is exhausted or until phase-out date, whichever comes first. | All devices must be in compliance by January 1, 2005. |
| Category III | October 1, 2002 for new installations. Existing devices may be used until service life is exhausted or until phase-out date, whichever comes first. Exceptions: (see below) | All devices shall meet NCHRP 350 compliance by January 1, 2006. |
| Category III Exception: Temporary Concrete Barriers - Type 4 (Obsolete) | Manufactured and purchased prior to October 1, 2002 may be used for temporary installations on projects advertised before 1/1/2006 but may NOT be used for permanent installations. | January 1, 2006 |
| Category III Exception: Temporary Concrete Barriers - New Standard: Type 7 F-shape | Units manufactured and purchased after October 1, 2002 must meet new standard. | N/A |
| Category III Exception: Truck-mounted Attenuators & Work Zone Crash Cushions | October 1, 1998 for new installations | NA |