March 18, 2005

REVISION OF SECTIONS 105 AND 618

CONTRACTOR SUBMITTALS

# NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.

Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on all projects.

March 18, 2005

REVISION OF SECTIONS 105 AND 618

CONTRACTOR SUBMITTALS

Sections 105 and 618 of the Standard Specifications are hereby revised for this project as follows:

In subsection 105.02, delete Table 105-1 and replace with the following:

# TABLE 105-1

SUMMARY OF CONTRACTOR SUBMITTALS

| SECTION NO. | DESCRIPTION | TYPE | CONTRACTOR P.E. SEAL REQUIRED? |
| --- | --- | --- | --- |
| 504 | MSE Walls (Contractor Alternative) | Shop Drawing | Yes |
| 504 | MSE Walls (Default Design) | Shop Drawing | No |
| 508 | Timber Structures | Shop Drawing | No |
| 509 | Steel Structures | Shop Drawing | No |
| 512 | Bearing Devices Type II | Shop Drawing | No |
| 512 | Bearing Devices Type III | Shop Drawing | Yes |
| 514 | Pedestrian and Bikeway Railing | Working Drawing | No |
| 518 | Expansion Devices: 0-100 mm (0-4”) | Working Drawing | No |
| 518 | Expansion Devices: 0-150, 225, 300… mm (0-6”, 9”, 12”…) | Shop Drawing | Yes |
| 601 & 618 | Precast Panel Deck Forms | Working Drawing | No |
| 601 | Permanent Steel Bridge Deck Forms | Working Drawing | Yes |
| 601 | Falsework | Working Drawing | Yes |
| 602 | Reinforcing Steel | Working Drawing | No |
| 606 | Bridge Railing | Working Drawing | No |
| 607 | Sound Barriers (Alternative) | Shop Drawing | Yes |
| 607 | Sound Barriers (Default Design) | Working Drawing | No |
| 613 | Light Standards (Low Mast) | Working Drawing | Yes |
| 613 | Light Standards (High Mast) | Working Drawing | Yes |
| 614 | Overhead Sign Structures | Shop Drawing | Yes* |
| 614 | Traffic Signal Pole (Mast Arm) | Shop Drawing | No |
| 614 | Traffic Signal Pedestal Pole | Working Drawing | No |
| 614 | Traffic Signal Equipment | Working Drawing | No |
| 614 | Variable Message Signs (Cabinet and tilting bracket) | Working Drawing | Yes |
| 618 | Prestressed Concrete (Pre-tensioned) | Shop Drawing | Yes* |
| 618 | Prestressed Concrete (Post-tensioned) | Shop Drawing | Yes* |
| 618 | Steel Diaphragms between Prestressed Girders | Working Drawing | No |
| 628 | Pre-fabricated Pedestrian Bridges | Shop Drawing | Yes |

*A PE seal is required where the Contractor has provided the design for the item, or performed engineering to modify the details shown on the plans.  The PE seal is not required where complete details are provided on the plans.

Subsection 618.04 (a) shall include the following:

##### Minor changes to design details or engineering drawings that do not represent a significant change to the original design will not require a Professional Engineer seal.  The Contractor shall submit supporting calculations for these changes along with the shop drawings.