March 18, 2005

REVISION OF SECTION 106

# CERTIFICATES OF COMPLIANCE AND

CERTIFIED TEST RESULTS

#### NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions regarding its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies that use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on all projects.

Section 106 of the Standard Specifications is hereby revised for this project as follows:

In subsection 106.09 delete the list following the first paragraph and replace with the following:

- The Department’s project number

- Manufacturer’s name

- Address of manufacturing facility

- Laboratory name and address

- Name of product or assembly

- Complete description of the material

- Model, catalog, stock number (if applicable)

- Lot, heat, or batch number identifying the material delivered

- Date(s) of the laboratory testing

- Listing of all applicable specifications required by the Department for this particular product or assembly. Certificates shall reference the actual tests conducted on samples taken from the same lot, heat, or batch, and shall include a statement that the product or assembly to be incorporated into the project was fabricated in accordance with and meets the applicable specifications.

- The following certification, signed by a person having legal authority to act for the Contractor:

I hereby certify under penalty of perjury that the material listed in this Certificate of Compliance represents __________ (quantity) of pay item __________ (pay item number and Description) for installation on project number __________________. _________________________ __________________ Contractor Date

Subsection 106.09 shall include the following:

The Certificate of Compliance shall be an original document, not a facsimile, with an original signature (including corporate title) by a person having legal authority to act for the manufacturer.  It shall state that the product or assembly to be incorporated into the project has been sampled and tested, and the samples have passed all specified tests.  One copy of the Certificate of Compliance shall be furnished to the Engineer at the time of material delivery. Failure to comply may result in delays to the project or rejection of the materials.

In subsection 106.10 delete the list following the first paragraph and replace with the following:

- The Department’s project number

- Manufacturer’s name

- Address of manufacturing facility

- Laboratory name and address

- Name of product or assembly

- Complete description of the material

- Model, catalog, stock number (if applicable)

- Lot, heat, or batch number identifying the material delivered

- Date(s) of the laboratory testing

- All test results are required to verify that the material furnished conforms to all applicable Department specifications. Test results shall be from tests conducted on samples taken from the same lot, heat, or batch.

- The following certification, signed by a person having legal authority to act for the Contractor:

I hereby certify under penalty of perjury that the material listed in this Certified Test Report represents __________ (quantity) of pay item __________ (pay item number and Description) for installation on project number __________________. _________________________ __________________ Contractor Date

Subsection 106.10 shall include the following:

The Certified Test Report shall be an original document, not a facsimile, with an original signature (including corporate title) by a person having legal authority to act for the manufacturer or the independent testing laboratory.  It shall state that the test results show that the product or assembly to be incorporated into the project has been sampled and tested, and the samples have passed all specified tests.  One copy of the Certified Test Report shall be furnished to the Engineer at the time of material delivery. Failure to comply may result in delays to the project or rejection of the materials.