###### April 7, 2006

# REVISION OF SECTION 630

##### Method of Handling Traffic

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions regarding its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies that use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on all projects.

April 7, 2006

REVISION OF SECTION 630

METHOD OF HANDLING TRAFFIC

Section 630 of the Standard Specifications is hereby revised for this project as follows:

In subsection 630.09 (8), delete Table 630-2 and replace with the following:

Table 630-2

## VERTICAL CLEARANCES TO STRUCTURES

|  | Highway Underpasses | Railway Underpasses | Overhead Wires |
| --- | --- | --- | --- |
| Local Rural Roads Local Urban Streets Rural Collectors Urban Collectors | 14 Feet | 23 Feet2 | 3 |
| Rural Arterial Urban Arterial Freeways | 16 Feet1 | 23 Feet2 | 3 |
| Vertical clearance to sign trusses and pedestrian overpasses shall be 17 feet. Measured from top of rail to bottom of highway structure. All railway clearances are subject to the individual railroad’s approval. Communication and power lines of: 0 to 750 volts 18 Feet 750 to 22,000 volts 20 Feet 22,000 to 50,000 volts 22 Feet For voltages over 50,000 volts, increase clearance ½ inch for each 1000 volts. |