June 29, 2006

REVISION OF SECTION 208

STORM DRAIN INLET PROTECTION

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use on projects having storm drain inlet protection devices.

June 29, 2006

REVISION OF SECTION 208

STORM DRAIN INLET PROTECTION

Section 208 of the Standard Specifications is hereby revised for this project as follows:

Subsection 208.01 shall include the following:

This work consists of the installation of pre-manufactured storm drain inlet protection at locations shown on the plans.

Subsection 208.02 shall include the following:

- Storm Drain Inlet Protection (Type I). Storm Drain Inlet Protection (Type I) shall consist of woven geotextile tubes that are capable of containing aggregate. The tubes shall have the following dimensions:

Diameter		4 inches

Section length		2 feet minimum

Fabric for the Storm Drain Inlet Protection shall have the following properties:

| Grab tensile strength | ASTM D 4632 | LBS | 90 minimum |
| --- | --- | --- | --- |
| Trapexoid Tear Strenght | ASTM D 4533 | LBS | 25 minimum |
| Percent Open Area | COE-22125-86 | % | 10 |
| Water Flow Rate | ASTM D 4491 | GAL/MIN/FT | 145 |
| Ultraviolet Resistance | ASTM D 4355 | % | 70 |

Storm drain inlet protection shall be capable of remaining in place during a storm event and have an approximate weight of 7 to 10 pounds per linear foot of device.  The device shall also be capable of conforming to the shape of the curb.  Aggregate contained in the storm drain inlet device shall consist of gravel or crushed stone conforming to Table 703-7 for Class C.

Subsection 208.05 shall include the following:

- Storm Drain Inlet Protection (Type I). Prior to installation, the Contractor shall prepare the surface of the areas in which the Storm Drain Inlet Protection devices are to be installed such that they are free of materials greater than 2 inches in diameter and are suitably smooth for the installation of the Storm Drain Inlet Protection, as approved.  The ends of the inlet protection shall extend a minimum of 12 inches past each end of the inlet.

Subsection 208.07 shall include the following

Storm Drain Inlet Protection will be measured by the actual number of linear feet that are installed and accepted.

Subsection 208.08 shall include the following:

# Pay Item														Pay Unit

Storm Drain Inlet Protection (Type I)			Linear Foot

Payment will be full compensation for all work, materials and equipment required to construct, maintain and remove the storm drain inlet protection upon completion of the work, including surface preparation.

Aggregate will not be measured and paid for separately, but shall be included in the work.