# Project special worksheet: 202rap

10-19-06

# REVISION OF SECTION 202

RECLAIMED ASPHALT PAVEMENT MILLINGS

Section 202 of the Standard Specifications is hereby revised for this project as follows:

Subsection 202.09 shall include the following:

CDOT will retain      ♦      of the Reclaimed Asphalt Pavement (RAP) millings removed from the existing mat on this project. All remaining RAP millings, if any, shall be used in the project as allowed in the Contract or as approved by the Engineer.  Otherwise, they shall become the property of the Contractor and shall be disposed at his expense outside the project limits.

If the Contractor desires to retain a quantity of RAP millings that exceeds that allowed by this Contract, the Contractor may request this by submitting a Value Engineering Change Proposal (VECP) in accordance with subsection 104.07.

For this project the RAP millings that CDOT will retain shall be delivered and stockpiled at the following locations:

▲

Subsection 202.12 shall include the following:

Unless otherwise specified in the Contract, the disposal and hauling of the RAP millings to other locations or its use on the project or at other locations will not be measured and paid for separately, but shall be included in the work.

INSTRUCTIONS TO DESIGNERS (delete instructions from final draft):

This Project Special Provision should be used on pilot projects as determined by the Region Materials Engineer.

♦ Designer should fill in appropriate percentage or tons of millings that CDOT would like to retain. This amount should be discussed with maintenance forces in the region.

▲ Designer should fill in address where RAP millings shall be delivered by the Contractor.