November 30, 2006

REVISION OF SECTION 101

FALSEWORK, FORMWORK AND SHORING

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in all projects.

# November 30, 2006

# REVISION OF SECTION 101

FALSEWORK, FORMWORK AND SHORING

Section 101 of the Standard Specifications is hereby revised for this project as follows:

Add subsection 101.89 as follows:

101.89 Falsework.  Falsework is temporary construction used to support structural elements of concrete, steel, masonry or other materials during their construction or erection until they become self-supporting.  Falsework may also be used to provide temporary support to elements of a structure during demolition or reconstruction.

Add subsection 101.90 as follows:

101.90 Formwork.  Formwork is the temporary structure or mold used to retain plastic or fluid concrete in its designated shape until it hardens.

Add subsection 101.91 as follows:

101.91 Shoring.  Shoring is temporary construction that is used to support the earth adjacent to excavation or embankment.