April 12, 2007

REVISION OF SECTION 212

SEEDING SEASONS

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in all projects having seeding

April 12, 2007

REVISION OF SECTION 212

SEEDING SEASONS

Section 212 of the Standard Specifications is herby revised for this project as follows:

In subsection 212.03 delete the seeding seasons table and replace it with the following:

| Zone | Spring Seeding | Fall Seeding |
| --- | --- | --- |
| Areas other than the Western Slope |
| Below 6000’ | Spring thaw to June 1 | September15 until consistent ground freeze |
| 6000’ to 7000’ | Spring thaw to June 1 | September1 until consistent ground freeze |
| 7000’ to 8000’ | Spring thaw to July 15 | August 1 until consistent ground freeze |
| Above 8000’ | Spring thaw to consistent ground freeze |
| Western Slope |
| Below 6000’ | Spring thaw to May 1 | August 1until consistent ground freeze |
| 6000’ to 7000’ | Spring thaw to June 1 | September 1 until consistent ground freeze |
| Above 7000’ | Spring thaw to consistent ground freeze |