April 12, 2007

REVISION OF SECTION 630

NCHRP 350 REQUIREMENTS

###### NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

# Use this standard special provision on all projects.

April 12, 2007

REVISION OF SECTION 630

NCHRP 350 REQUIREMENTS

Section 630 of the Standard Specifications is hereby revised for this project as follows:

In subsection 630.08, delete the second paragraph and replace with the following:

Category IV devices will not be required to meet NCHRP 350 requirements.  All other work zone devices that do not meet NCHRP 350 requirements shall not be used.

Except for Category IV devices, the Contractor shall obtain and present to the Engineer the manufacturer’s written NCHRP 350 certification for each work zone device before it is first used on the project.