June 7, 2007

REVISION OF SECTION 630

MOBILE PAVEMENT MARKING ZONE

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use on projects that ½ mile or longer as determined by the Region Traffic Engineer.

Use the “lump sum” pay item for region-wide projects and the “day” pay item for long corridors.

June 7, 2007

REVISION OF SECTION 630
MOBILE PAVEMENT MARKING ZONE

Section 630 of the Standard Specifications is hereby revised for this project as follows:

Subsection 630.01 shall include the following:

This work consists of furnishing a mobile pavement marking zone for the application of pavement marking materials.

Subsection 630.09 shall include the following:

The Contractor's Method of Handling Traffic (MHT) shall include details of a mobile pavement marking zone.  The mobile pavement marking zone shall include, as a minimum, three operations groups as follows:

(1)	The application group composed of the pavement marking application truck and at least one cone installation truck.

(2)	The pick-up group composed of at least one truck for warning and one truck for cone pickup.

(3)	The signing group composed of one or more trucks installing signs. At a minimum, the following signs shall be used as required:

HIGHWAY/PAINTING/NEXT     MILES	60 inch by 36 inch

HIGHWAY/PAINTING/AHEAD		 	48 inch Diamond

SPEED/LIMIT					 		48 inch by 60 inch

Truck mounted message boards may be used in lieu of temporary signs.

Groups 1 and 2 shall each be equipped with a truck-mounted ADVANCE WARNING FLASHING OR SEQUENCING ARROW PANEL (C TYPE).   Truck-mounted impact attenuators shall be used and shall be certified by the manufacturer to be able to withstand a 62 MPH impact in accordance with NCHRP 350, Test Level 3.    The cone setting truck and the cone pick-up truck shall not be the same vehicle.

Group 2 shall also be equipped with a truck mounted NO/PASSING/THRU/PAINTING/ZONE 48 inch by 60 inch sign.

Group 3 shall place HIGHWAY/PAINTING/AHEAD signs on intersecting crossroads and interchange entrance ramps as the pavement marking operation approaches. If required for spot locations, this group shall also provide flagging.

All groups shall maintain radio communications to assure appropriate advance warning and buffer distances are maintained for traffic.

All groups shall clear the roadway every 15 minutes or as deemed necessary by the Engineer to allow traffic queues to pass.

Traffic cone spacing shall be determined as required by the standard plans calculations based on current speed limits. Cone spacing shall not exceed 120 feet.  Cones shall be placed a distance of 2 miles on the centerline. The distance and spacing may be adjusted, depending on traffic conditions and terrain, as determined by the Engineer.

June 7, 2007

2

REVISION OF SECTION 630

MOBILE PAVEMENT MARKING ZONE

Subsection 630.14 shall include the following:

Mobile pavement marking zone will not be measured, but will be paid for as a single lump sum, or by the actual number of days that it is utilized.   Flagging will be measured and paid for separately in accordance with Section 630.

Subsection 630.15 shall include the following:

Pay Item								Pay Unit

Mobile Pavement Marking Zone			Lump Sum

Mobile Pavement Marking Zone			Day

Traffic Control Management, vehicles, traffic control devices, and all other work, materials and equipment necessary to complete the item will not be measured and paid for separately but shall be included in the work.