###### July 3, 2008

REVISION OF SECTION 106

Hot Mix Asphalt Test Result Verification

and Dispute Resolution

##### NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction.  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on projects having more than 5000 tons of HMA.

.

Section 106 of the Standard Specifications is hereby revised for this project as follows:

Subsection 106.05 (b) shall include the following:

If the Contractor elects to question the Hot Mix Asphalt (HMA) acceptance test results, the steps outlined in CP 17 shall be followed.  The results from the CP 17 resolution process shall be binding on both the Department and the Contractor.  Requests for CP 17 process for all elements except density shall be submitted in writing to the Engineer a minimum of five working days of the Contractor receiving acceptance test data from the Engineer.  The specific element questioned shall be identified in writing.  All requests for the CP 17 process for the density element shall be submitted in writing to the Engineer within 24 hours of receiving test data from the Engineer.

The Contractor shall have the option of selecting either the CDOT Materials and Geotechnical Branch or a consultant laboratory not associated with the project  to perform the third party testing.  The Contractor shall document his choice in writing at the Pre-Paving Conference.  In the event a consultant laboratory is chosen, the CDOT Materials and Geotechnical Branch will determine the consultant that will be used from a pre-established list and ensure there is no conflict of interest.

In the event third party testing is required, the responsibility for the testing expenses shall be assigned in accordance with CP 17.  The costs for testing are shown in Table 106-4. An administrative cost of $230 per sample will be charged in addition to the costs shown.

Table 106-4

Costs for Third Party Testing

| Test | Cost |
| --- | --- |
| AC Ignition Correction | $318 |
| AC Nuclear Correction | $373 |
| AC content by Ignition | $109 |
| AC content by Nuclear | $86 |
| Gradation | $115 |
| Mixture Volumetrics (Rice, Air Voids,VMA) | $338 |
| Core Bulk Specific Gravity | $32 |
| Lottman | $379 |