Department of Transportation

Project Development Branch

Standards and Specifications Unit

4201 East Arkansas Avenue, Room 290

Denver, Colorado  80222

(303) 757-9040  FAX:(303)757-9820

MemoranduM

DATE:		November 5, 2009

TO:		All Holders of Standard Special Provisions

FROM:		Larry Brinck, Standards and Specifications Engineer,

Project Development Branch

SUBJECT:	Revision of Sections 105, 202, 401, 406, and 601, Hot Mix Asphalt Pavement Roadway Smoothness (High Speed Profiler)

As of this date, our unit is issuing a revised version of the standard special provision, Revision of Sections 105, 202, 401, 406, and 601, Hot Mix Asphalt Pavement Roadway Smoothness (High Speed Profiler).  This new standard special is 9 pages long and is dated November 5, 2009.  Use this standard special in projects having hot mix asphalt.  This standard special will be required in projects that are advertised on or after December 3, 2009.  But, feel free to use this standard special before this date.

This revised standard special provision replaces one having the same name, dated July 3, 2008.  The following are modifications contained in this revised version:

- Heating and Remixing has been removed from % improvement criteria to the “don’t make it worse” criteria.

- The default smoothness category for HMA pavement smoothness is HRI Category II.

- Contractors can now grind areas requiring corrective work prior to pavement smoothness acceptance testing.

- Addition of areas that can be tested with the HSP including 12 ft+ lanes, ramps, acceleration … lanes.

- An additional 5 ft outside the paving limits will be tested for localized roughness to help ensure smooth transitions.

- HRI % Improvement (Rural) can now be changed to HRI Category I at anytime prior to final smoothness acceptance testing.

- Valve boxes are no longer excluded, but if an area of localized roughness has a valve box and it is less than 25 feet long, that area will be tested with a 10 ft straight edge for corrective work.

- Clarified the criteria for pavement smoothness verification

- Clarified that the “don’t make it worse” criteria does not apply when the surface treatment will be overlaid.

Those of you who keep books of standard special provisions should replace the obsolete version of this standard special provision with this one.  A new index of Standard Special Provisions, dated November 5, 2009, is attached.

mrs/lb

Attachment

Distribution: Per Distribution List