October 21, 2010

REVISION OF SECTION 630

STACKABLE CHANNELIZERS

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in projects having stackable vertical channelizers or tubular markers.

October 21, 2010

REVISION OF SECTION 630

STACKABLE CHANNELIZERS

Section 630 of the Standard Specifications is hereby revised for this project as follows:

Add subsection 630.061, immediately following subsection 630.06, as follows:

630.061 Temporary channelizing devices.

- Stackable Vertical Panels.  Stackable vertical panels shall meet the NCHRP 350 crash test requirements and shall meet MUTCD requirements for vertical panels.  The stackable vertical panels shall have the following properties:

| Property | Specification |
| --- | --- |
| Panel Material | Low density polyethylene |
| Color | Orange and white stripes with orange or white frame and black ballast |
| Vertical Panel Height | 24, 36, 42 in. |
| Ballast Type* | Rectangular or Square |
| Ballast Weight* | 9 - 30 lbs |
| * NOTE: The ballast type and weight shall be as shown in the contract or as approved by the Engineer. |

Markings for vertical panels shall be alternating orange and white retro-reflective stripes, sloping downward at an angle of 45 degrees in the direction of vehicular traffic.  The width of the stripes shall conform to the requirements of the MUTCD.

New Vertical Panels shall be retroreflectorized with Type IV Sheeting. Existing Vertical Panels manufactured with Type III sheeting may be used on projects advertised prior to January 1, 2014.  Vertical Panels used on projects advertised on or after January 1, 2014 shall be manufactured with Type IV sheeting.   The stackable vertical panels shall be selected from the Department’s Approved Products List and shall have a smooth, sealed outer surface that will display the same approximate color day and night.

- Stackable Tubular Markers. Stackable tubular markers shall meet NCHRP 350 crash test requirements and shall conform to MUTCD requirements for Tubular Markers.  The stackable tubular markers shall have the following properties:

October 21, 2010

2

REVISION OF SECTION 630

STACKABLE CHANNELIZERS

| Property | Specification |
| --- | --- |
| Tubular Section | Low density polyethylene |
| Color | Orange Tubular Marker with Black Base |
| Height (min.) | 42 in |
| Ballast Type* | Rectangular, Octagonal or Square |
| Ballast Weight* | 15 - 40 lbs. |
| * NOTE: The ballast type and weight shall be as shown in the contract or as approved by the engineer. |

New Tubular Markers shall be retroreflectorized with Type IV Sheeting.  Existing Tubular Markers manufactured with Type III sheeting may be used on projects advertised prior to January 1, 2014.  Tubular Markers used on projects advertised on or after January 1, 2014 shall be manufactured with Type IV sheeting. The stackable tubular markers shall be selected from the Department’s Approved Products List and shall have a smooth, sealed outer surface that will display the same approximate color day and night.

Subsection 630.15 shall include the following:

Payment will be made under:

Pay Item																		Pay Unit

Stackable Vertical Panel														Each

Stackable Tubular Marker														Each