Pilot project special provision:  630atce

7.10.2009

Revision of Section 630

ADDITIONAL TRAFFIC CONTROL EMPLOYEE

Section 630 of the Standard Specifications is hereby revised for this project as follows:

Subsection 630.10, after the first paragraph, shall include the following:

The Contractor shall provide a minimum of one additional employee to assist each Traffic Control Supervisor required for the project in performing traffic control management.  Each of these additional employees shall be provided with his own truck for use on the project. These additional employees shall perform traffic control related duties as assigned by the TCS.  These additional employees shall be certified as flaggers so that when not directly assisting the TCS, they may provide flagger breaks.  For the sake of wages on Federal Aid Davis Bacon projects the additional employees shall be paid the wage appropriate to the type of work they are performing on the project.

Subsection 630.10, third paragraph, immediately following the first sentence, shall include the following:

A minimum of one Traffic Control Supervisor and additional employee shall be on site at all times when active traffic control activities in accordance with an approved MHT are underway.

In subsection 630.14, sixth paragraph, delete the first two sentences and replace with the following:

The quantity to be measured for Traffic Control Management will be the number of 24-hour days of active TCM performed by one or more Traffic Control Supervisors with additional employees. Payment will be made for one day of Traffic Control Management regardless of the number of Traffic Control Supervisors with additional employees required to adequately control the work for that 24-hour period.

Subsection 630.15 shall include the following:

Payment for Traffic Control Management will be full compensation for all work and materials required to complete the item, including the actual number of Traffic Control Supervisors with additional employees required by the Contractor’s phasing and all vehicles required for the Traffic Control Supervisors and additional employees.  Flagging breaks provided by the additional employees will not be measured and paid for separately, but shall be included in the work.

*******************************************************************************************

INSTRUCTIONS TO DESIGNERS (delete instructions and symbols from final draft):

This is a pilot project special provision that is to be used only on selected projects.  Submit proposed pilot projects to the Standards & Specifications Unit for review prior to using this special provision.