ARCHAEOLOGY AND HISTORY

##### Introduction

Section 106 of the National Historic Preservation Act (NHPA) sets forth the process that Federal agencies must follow when planning undertakings that have the potential to affect historic properties.  As stated in the introduction of the regulations:

Section 106 of the NHPA requires Federal agencies to take into account the effects of their undertakings on historic properties and afford the Advisory Council on Historic Preservation (ACHP) a reasonable opportunity to comment on such undertakings. [36 CFR Part 800, Section 800.1]

The Federal agency with jurisdiction over an undertaking is responsible for complying with Section 106.  For most CDOT projects, this agency is FHWA.  The Federal Highway Administration has authorized CDOT to conduct cultural resource surveys, recommend determinations of eligibility and effect, and consult directly with the SHPO.  FHWA is legally responsible for the findings and determinations made during the Section 106 process, and also determines whether the work done by CDOT fulfills the intent of the legislation.  FHWA is also responsible for ensuring the Section 106 process is undertaken with enough time to plan for public coordination and SHPO review of a broad range of alternatives.  Otherwise, the agency may be unable to document that it has fulfilled its responsibilities under Section 106.

Any formal coordination with the Advisory Council on Historic Preservation (ACHP) is completed through FHWA (or other federal agency with jurisdiction over an undertaking).  Whenever a project is determined to have adverse effects to historic properties, FHWA must notify the ACHP, and in specific circumstances, invite the ACHP to take part in consultation regarding these properties (requiring more time to process a clearance).  The ACHP will become formally involved in the review of the following types of projects:

- Projects with substantial impacts on important historic properties (including National Historic Landmarks, which also involve coordination with the National Park Service).

- Projects with important questions of policy or interpretation of the Section 106 regulations.

- Projects with the potential for procedural problems, public controversy, or litigation.

- Projects of concern to American Indian tribes.

Federal Laws and Regulations

National Environmental Policy Act of 1969 (NEPA); Antiquities Act of 1906; National Historic Preservation Act of 1966, (as amended); National Register of Historic Places Act, 36 CFR 60; Determination of Eligibility, 36 CFR 63; Advisory Council on Historic Preservation regulations, 36 CFR 800; Executive Order 11593, Protection and Enhancement of the Cultural Environment; Native American Graves Protection and Repatriation Act (NAGPRA) (as amended).

State laws and regulations:  Colorado Register of Historic Places of 1975, CRS 24-80.1; Historical, Prehistorical, and Archaeological Resources Act of 1973.

## Process for Requesting and Completing Historical Resource Clearances

Region Planning and Environmental Managers (RPEMs) are encouraged to contact the Staff Historian as early as possible to discuss undertakings that have the potential to impact historic properties, objects, or structures.  It is important to identify potential historic resources early in the planning phase to allow enough time for coordination with regulatory agencies and other interested parties.  Section 106 requires coordination with local historic preservation commissions if they have jurisdiction within the project area, in addition to public notification.

Potential historic resources are those that are fifty years or older; however, resources less than 50 years old are surveyed if considered to have exceptional significance or can contribute significant information to the historical record.  Typical historic resources include buildings, residential neighborhoods, commercial districts, agricultural complexes, bridges, canals, ditches, reservoirs and railroad lines.  Less obvious resources include structure foundations, trails, sidewalks, and landscapes, including vegetation and dumps.  RPEMs should notify the Staff Historian if a project has the potential to affect historic resources—generally projects that require right-of-way where buildings, ditches, railroad lines, or similar features are located.

Definition of “Undertaking”

For transportation projects, an undertaking is typically defined as any construction, maintenance, enhancement, or planning project with the potential to impact historic resources.  This includes:

- The taking or alteration of all or part of a building, structure, or property 50 years of age or older.

- Ground disturbance in the vicinity of historic properties.

- Changes in appearance, noise levels, or visual characteristics in the vicinity of historic properties.

- Transfers requiring lease or sale of a property.

Any time a project will have direct or indirect impacts to potentially historic resources, whether within public right-of-way or on private land, an historical clearance should be discussed with the Staff Historian.

## Programmatic Agreements, Memoranda of Understanding, and When They Are Used

The Cultural Resource Section currently has three different agreements outlining program alternatives for specific projects or circumstances under which projects with the potential to impact historic resources do not require SHPO concurrence.  Refer to the Environmental Guidance notebook for the text of these agreements.

## Minor Highway Improvement Projects

This agreement was signed in 1991 by the ACHP, FHWA, Colorado SHPO, Colorado State Archaeologist and CDOT.  It specifies certain project types that have been determined to cause no effect to historic resources and will therefore not require coordination with the SHPO and ACHP.  Typical projects include curb and gutter, guardrail installation, lighting and signalization, improvements at railroad crossings, minor widening of structures over historic linear features, paving of gravel shoulders, overlay and sealcoats, bridge deck rehabilitation (non-historic only), certain highway intersection improvements and minor widening projects.  There are exceptions to these project types so the Staff Historian must always be contacted to determine if this agreement applies.

## Section 106/State Register Act Procedures

This Memorandum of Understanding was signed in 1996 by the SHPO and CDOT.  The agreement outlines the procedures to be followed in order to increase the efficiency of the Section 106 and State Register Act clearance process for history (note: archaeology is not covered by this agreement).  In certain circumstances, to be determined by the Staff Historian, coordination with the SHPO will not be required.  The Staff Historian is also able to determine the scope and type of survey required based on the magnitude of the project, and can make determinations of eligibility and effect without consultation from the SHPO under certain conditions.  This agreement does not apply to projects completed by consultants.

## Historic Bridges

An agreement regarding the disposition of historic bridges was signed in 1988 by the SHPO and CDOT.  The agreement was updated at the conclusion of the Historic Bridge Survey in 2001, though it was not altered significantly.  The Memorandum of Understanding makes eligibility determinations for all vehicular bridges and outlines the protection procedures for bridges determined eligible for the National or State Registers of Historic Places.

The Staff Historian will determine when these agreements should be utilized.  If one of these agreements can be applied to a project, the Historian will write a memo to the RPEM explaining why the agreement applies and the terms of the clearance.  This memo serves as the clearance required for historic resources, a process that usually takes one to two weeks.  If a project does not meet these circumstances, additional research will be required to process the project under the terms of Section 106.

## Information Required to Initiate an Historical Clearance

- Detailed project description, including:

- Project title, number, subaccount, function, or other accounting numbers

- Project limits (i.e., amount of land to be surveyed on either side of the centerline, milepost limits, etc.)

- Project location map

- Design plans (if available)

- Copy of the 128/463, memos, or other documents describing the project

- Brief description of resources to be impacted, i.e., CDOT structure numbers and locations, or description of ditch, farm house, neighborhood, etc.

- Project Schedule, with estimates of FIR, FOR, and AD dates.

- Written memo or telephone conference with the Staff Historian describing concerns about potentially historic resources or other project related issues.

Process for Requesting and Completing Archaeological Resource Clearances

At the earliest possible date in the planning process for a proposed undertaking, the RPEM should forward to the Staff Archaeologist a written request for an archaeological clearance.  Undertakings include, but are not limited to, highway construction projects, off-system roadway projects, maintenance activities, transportation enhancements, and property transfers or sales.  Archaeological investigations initiated by private contractors for activities associated with CDOT projects–such as undesignated material sources and equipment staging areas–are the responsibility of the contractor.  It is imperative that project managers and contractors are made aware of their responsibilities in this regard, and that all appropriate permits and clearances are obtained prior to initiating ground disturbance for any activity peripheral to actual construction.

##### Information Required to Initiate an Archaeological Clearance

- Project number and name.

- Subaccount number.

- Brief description of the project.

- Physical dimensions of the study corridor, including beginning and ending mileposts and corridor width.

- A copy of a 7.5 minute USGS topographic quadrangle or county map clearly showing the extent of the proposed undertaking, and engineering design plans, if available.

- In order for a clearance to be provided in a timely manner, a specific due date must be furnished.

- If temporary or permanent easements beyond the existing right-of-way are required to accommodate detours, line-of-sight improvements, shoulder widening or material source areas (among others), this should be noted and right-of-entry forms obtained and forwarded to the Staff Archaeologist.  CDOT Forms 128 and 463 can also be provided, but it is important to note that these forms do not by themselves constitute an adequate clearance request.

- Field and archival investigations should generally be scheduled for completion by the Field Inspection Review.

Scheduling of archaeological fieldwork should take into consideration seasonal conditions.  Projects with winter due dates should be requested in the summer or early fall.  Although field surveys can be conducted in many parts of the state throughout the year (weather permitting), even a thin blanket of snow can potentially terminate inventory plans.

##### Initial Consultation

If a project area is located partially or entirely on lands administered by a federal land managing agency such as the US Forest Service or Bureau of Land Management, the Staff Archaeologist will initiate consultation with that agency.  In many instances the federal agency will take the lead on cultural resource issues, in which case all Section 106 administrative responsibilities and obligations will be completed by that agency, even though CDOT will conduct archival and field research.

Although the SHPO generally does not require initial consultation on archaeological projects, larger and/or more complex undertakings may require SHPO involvement in determining the Area of Potential Effect (APE).  If a project is located on Indian reservation land, the Tribal Historic Preservation Officer (THPO), if designated, may formally assume responsibilities of the SHPO.  The SHPO/THPO has 30 days in which to respond to a request for consultation.  Tribal groups sometimes attach religious and cultural significance to properties beyond reservation boundaries, and these tribal entities—in addition to local governments, the general public and other specific interested parties—also have a right to consult about heritage resource issues in the context of Section 106 and NEPA (see “Native American Consultation” subsection, below).

Contact with the Advisory Council on Historic Preservation (ACHP) is generally unnecessary as part of the initial archaeological consultation process.  ACHP consultation is sought for undertakings involving federal funds, properties or permits, and usually only when historic or archaeological properties will be adversely affected.

When consulting firms contract with CDOT Regions to conduct archaeological investigations, the Staff Archaeologist must be informed of the name and qualifications of the firm.  The CDOT Archaeologist will initiate consultation with the SHPO/THPO and any appropriate federal agencies regarding the nature and extent of the consultant’s proposed work.

## The Section 106 Process

The Section 106 regulations and guidance materials describe a four-step process agencies must follow to assess the eligibility of historic properties and potential impacts to these properties.  The cultural resource surveys for CDOT undertakings typically accomplish multiple steps (determinations of eligibility and effect as well as preliminary recommendations for mitigation of adverse effects) under one transmittal letter to the SHPO.  (Note that this generally entails one letter each for archaeology and history, although they may be combined as a situation dictates.)  The regulations recognize that agencies can conduct consultation on several steps at one time, as long as the process includes adequate time to consider the views of interested parties and the public.

The following are average time frames for completion of the Section 106 process, from notification to completion, if all necessary information is provided in a timely manner and there are no problems.  (Note: these time frames do not include Section 4(f) evaluations, which are detailed in a separate chapter.)  The effects determinations are explained in detail below.

Adverse Effect – six months or more

No Adverse Effect – four months

No Effect – two months

If time and schedules allow, the Staff Historian and/or Staff Archaeologist will conduct a pedestrian survey, as appropriate, and prepare the necessary paperwork.  Otherwise the project may be referred to the cultural resources consultant under contract to the Environmental Programs office.  For historical clearance work the region also may hire a consultant independently, in consultation with the Staff Historian.  Agency coordination involves completing a survey, preparing letters, and forwarding documentation to the SHPO, Advisory Council, FHWA, or other agencies, where necessary.  Meetings with the SHPO will be scheduled as needed by the Staff Historian, and on rare occasions, by the Staff Archaeologist.  Copies of all correspondence will be forwarded to the RPEMs for their files.

STEP 1: Initial Consultation with Participants in Section 106

The RPEM should notify the Staff Historian and/or Staff Archaeologist if he or she is aware of any parties with an interest in the undertaking. The Staff Historian/Staff Archaeologist will contact the members of local historical societies, museums, commissions, or other knowledgeable individuals who might be able to provide views or comments on an undertaking or have specific knowledge concerning historic properties.  Notification of the public and/or historic preservation organizations and individuals will occur commensurate with the type of undertaking, its anticipated effects on historic properties, and the level of federal involvement.

## STEP 2: Identification of Historic Properties

This step determines whether any resources that may be affected by an undertaking have the potential to be eligible for or listed on the National or State Registers of Historic Places.  It is not necessary for a resource to be listed on the National Register to be afforded protection under the terms of Section 106; eligible properties are also covered under federal and state legislation.

Eligible National Register resources must meet certain criteria, including association with significant events or people; technological, engineering, or architectural significance; or the ability to yield information about a prehistoric or historic site.  In addition to meeting the significance criteria, a resource must retain physical integrity or be able to demonstrate or communicate the qualities of its significance.  Except under exceptional situations, cemeteries, birthplaces, churches, structures that have been moved from their original location, reconstructed structures, memorial or commemorative structures, and structures less than 50 years old, are not considered eligible to the National Register.  Isolated artifacts and features also are generally evaluated as not NRHP eligible.

If a property is determined not eligible to the National Register, the Section 106 process is completed.  However, even though a property may not have enough significance or integrity to be nationally eligible, it can still be eligible for or listed on the State Register of Historic Places.  If so, it must be considered under the State Register Act.  In addition, some local governments in Colorado have historic preservation ordinances and/or lists of local landmark districts and properties.  Some properties may be listed as locally significant, and impacts to these resources must be coordinated with the local government.

- Determine Undertaking’s Area of Potential Effects (APE)

The Staff Historian, Staff Archaeologist or cultural resource consultant is responsible for determining and documenting the APE for each project.  The APE is defined as:

The geographic area or areas within which an undertaking may directly or indirectly cause changes in the character or use of historic properties, if any such properties exist.  The area of potential effects is influenced by the scale and nature of an undertaking and may be different for different kinds of effects caused by the undertaking.  [800.16 (d)]

The APE is not determined on the basis of land ownership and does not end at the highway right-of-way boundary.  The APE includes:

- All alternatives being considered for the undertaking.

- All locations threatened with ground disturbance.

- All locations from which the undertaking may be visible or audible.

- All locations where the undertaking may result in changes in traffic patterns, land use, public access, etc.

- All areas where there may be indirect as well as direct effects.

An APE is determined according to specific project circumstances.  All potentially historic properties within the APE must be taken into account when assessing project impacts.

- SHPO Concurrence on Determinations of Eligibility

Once potentially historic properties are identified within the APE, the Staff Historian, Staff Archaeologist or cultural resource consultant evaluates each property for historical or archaeological significance and recommends whether or not the property is eligible to the National or State Registers.

If it is determined that no historic properties exist within the APE, or that historic properties exist but will not be impacted by the work, and the SHPO concurs with this determination, the resulting determination is “no historic properties affected,” and the Section 106 process is completed.  If eligible properties exist and there is potential for impact to these properties, the Staff Historian/Archaeologist or consultant continues to Step 3.

According to the regulations, the SHPO has 30 days from receipt of the documentation to provide comments to CDOT.  If they do not submit their comments within the 30-day period, CDOT is authorized by the regulations to assume SHPO concurrence.  If the SHPO does not participate within the specified time frame for one phase of a project (i.e., eligibility determination), that does not preclude their participation in further phases of a project (i.e., determinations of effect, consultation, and final review of NEPA documentation).

## STEP 3: Assessment of Adverse Effects

During this step, the Staff Historian/Archaeologist or cultural resource consultant applies the criteria of adverse effect to any eligible or listed historic properties within the APE.  This process involves consultation with the SHPO as well as with interested parties that may have been identified during Steps 1 or 2.  Effects include direct or physical impacts to historic properties, as well as indirect impacts such as noise, visual, or atmospheric elements that may diminish a property’s integrity or alter the qualities that make it eligible to the National Register of Historic Places (NRHP).

###### No Adverse Effect and Adverse Effect

An adverse effect is found when an undertaking may alter, directly or indirectly, any of the characteristics of a historic property that qualify it for inclusion in the National Register in a manner that would diminish the integrity of the property’s location, design, settling, materials, workmanship, feeling, or association.  [800.5 (a) (1)]

Adverse effects include, but are not limited to:

- Physical destruction or damage to all or part of a property.

- Alteration of a property not consistent with the Secretary’s Standards for the Treatment of Historic Properties [36 CFR part 68].

- Removal of the property from its historic location.

- Change of the character of the property’s use or physical features within the property’s setting that contribute to its historic significance.

- Introduction of visual, atmospheric or audible elements that diminish integrity of the property’s significant historic features.

- Neglect of a property.

- Transfer, lease, or sale of a property out of Federal ownership or control without adequate and legally enforceable restrictions or conditions to ensure long-term preservation of the property’s historic significance [800.5 (a) (2) (i-vii)].

The finding of no adverse effect can be applied when an undertaking’s effects do not meet the criteria of adverse effect but are still considered to have an effect on a property.  This finding can also be applied when specific conditions are met to avoid adverse effects.

If SHPO concurs with the finding of no adverse effect, CDOT may proceed with the undertaking and the Section 106 process is completed.  The ACHP will not review findings of no adverse effect, except under unusual circumstances.  If the SHPO fails to respond within 30 days of their receipt of the finding, CDOT may assume SHPO concurrence with the finding and proceed with the project.

If the determination results in a finding of adverse effect, CDOT must proceed to Step 4 and consult further with the SHPO and other interested parties to resolve or mitigate adverse effects to historic properties.

## STEP 4: Resolution of Adverse Effects

The purpose of this step is to develop strategies that avoid, minimize, or mitigate adverse impacts to historic properties but also meet the basic objectives of all interested stakeholders.  Measures to mitigate negative impacts to historic resources include adjusting the proposed alignment to avoid impacting the resource, moving the resource to a new location (which generally does not apply to archaeological localities), and, as a last resort, photographic and written recordation of the resource prior to demolition.   Ideally, alternatives that avoid historic properties will have already been considered prior to this step.

FHWA notifies the ACHP of an adverse effect determination and provides specific documentation for their review of the project.  The ACHP is given 15 days from receipt of the documentation to determine whether or not they will participate in a project.  If a response is not received within that time frame, the agency continues the consultation without the involvement of the ACHP.  In addition, FHWA must invite the ACHP to participate in the consultation of adverse effects when:

- FHWA wants the ACHP to participate (i.e., for very controversial or high-profile projects).

- The undertaking will have an adverse effect on a National Historic Landmark.

- The project will result in the preparation of a Programmatic Agreement (a document intended to address adverse effects for complicated projects or for repetitive projects that result in expected outcomes).

## Preparing a Memorandum of Agreement (MOA)

To resolve adverse effects to historic properties, interested parties develop a Memorandum of Agreement (MOA) outlining agency responsibilities to avoid, minimize, or mitigate adverse effects.  Significant archaeological sites, which previously were exempt from this process, are now subject to development of an MOA prior to large-scale data recovery excavations.  If the ACHP decides to join the consultation, the MOA is executed with its participation.  If not, the agreement is developed and executed by FHWA and SHPO, with CDOT as an invited signatory.  In addition, the agencies or entities may invite other organizations (i.e., Indian tribes) to participate as invited signatories in the development of an MOA if those agencies will assume a specific role or responsibility as outlined in the MOA.

The execution and implementation of the stipulations in the MOA provides evidence of FHWA’s compliance with Section 106.  The MOA is submitted to the ACHP for filing, and CDOT, on behalf of FHWA, ensures the mitigation stipulations are carried out in accordance with the MOA.  Unless project circumstances change and other potentially historic properties will be affected by an undertaking, or CDOT/FHWA are unable to fulfill the stipulations of the MOA, the Section 106 process is considered complete.

## Requirements for Consultants Conducting Historic and Archaeological Resource Surveys

All consultants are expected to perform a field survey of the project area in accordance with the Secretary of Interior’s Standards for Archaeology and Historic Preservation and the Cultural Resource Report Forms and Guidelines developed by the Office of Archaeology and Historic Preservation (OAHP).  Sample historical and archaeological survey reports are included in Appendix ___.  Consultants should expect to attend a pre-field meeting with CDOT representatives to discuss the project, either at a CDOT office or by telephone.  They are required to conduct an OAHP file search prior to field investigations and review all pertinent maps and written information pertaining to previous inventories and documented sites, if applicable.  In most cases, all sites surveyed will be recorded in their entirety, even if they extend beyond the limits of the project area.  For historic sites (generally not including historic archaeological sites), consultants might need to discuss survey results and preliminary determinations of eligibility with OAHP staff prior to submitting the survey report in order to confirm that all pertinent information has been collected for the survey.  The CDOT Staff Historian will not need to attend this meeting unless required by unusual situations.  In most cases, the consultant is responsible for assessing effects to historic and archaeological resources if plans and designs have been created for specific transportation projects in the project area.  The assessment of effects should be undertaken in close consultation with the Staff Historian and/or Staff Archaeologist.

Consultants should submit all documents generated by the survey directly to the Staff Historian or Staff Archaeologist, as appropriate, who is responsible for direct coordination with the SHPO.  Where a federal land managing agency has assumed the duties of “lead agency” for a project, the Staff Historian/Archaeologist will forward all documentation to that agency, which will review the findings and subsequently send it to the SHPO.  Under no circumstances should the consultant send final documents or correspondence regarding specific projects directly to the SHPO.

## Required Documentation for Historic and Archaeological Surveys

Consultants conducting field surveys must submit the following documentation:

- Historic and/or Archaeological Resource Survey Report, formatted according to OAHP guidelines, documenting survey of prehistoric or historic resources encountered in the project area, including recommendations of National or State Register eligibility for each resource.  Consultants will provide three copies of the survey report (bound copies for history, bound or unbound for archaeology) that include OAHP inventory forms, in addition to at least one copy of the survey report without inventory forms for submittal to OAHP (or other federal agencies with jurisdiction over the undertaking, if needed).  Site forms should not be included in bound archaeology report copies.  All reports, site forms and other documentation must be printed double-sided whenever possible; single-sided copies are unacceptable, unless previous notification to this effect has been made to CDOT.

- For archaeological surveys, 7.5’ USGS topographic quadrangles (or photocopied portions thereof) with the survey area clearly marked, and separate quad maps (generally as a report appendix) showing the location of all cultural resources present in the survey area.

- For historic surveys, USGS quad maps or project maps that clearly define the Area of Potential Effect determined for the survey.  The consultant should also provide an explanation of the APE boundaries and why these boundaries were chosen, taking into account direct and indirect impacts.

- OAHP Inventory Record Forms, including original black and white photographs of historic resources over 50 years of age, and/or color photographs of archaeological resources, with significance statements and eligibility recommendations.

- For historic surveys, Draft Determination of Eligibility and Effects letter (if required by terms of contract) to SHPO on 3.5” diskette in Corel WordPerfect or Microsoft Word format.  Samples of these letters are available from the Staff Historian.

Consultant Minimum Qualifications

- All tasks must be performed under the direct supervision of an individual meeting the criteria established under the Secretary of the Interior’s Standards for Archaeology and Historic Preservation.

- Consultants must have documented experience in completing historical or archaeological studies (as appropriate) under the requirements of Section 106 of the National Historic Preservation Act (NHPA) and the State Register of Historic Places Act.

- Consultants must have direct experience working with the Colorado State Historic Preservation Officer (SHPO) on cultural resource surveys and project coordination.

- Archaeological consultants must possess a current State of Colorado Archaeological Survey and Testing Permit.  When applicable, permits must also be obtained prior to project initiation from federal land managing agencies and Indian tribes.

- All archival, field and laboratory investigations and resulting documentation will follow SHPO/THPO guidelines and other state and federal specifications, as appropriate.

Native American Consultation Procedures

As stipulated in the National Historic Preservation Act of 1966 (as amended) and the revised Advisory Council on Historic Preservation regulations (36 CFR 800), federal agencies must afford the Native American community a reasonable opportunity to comment on and participate in federal undertakings in the context of the Section 106 process.  According to 36 CFR 800.2(c)(2)(ii), the “…agency official [must] consult with any Indian tribe…that attaches religious and cultural significance to historic properties that may be affected by an undertaking, …regardless of the location of the historic property [on or off tribal lands].”  Because federally recognized tribes are by law considered sovereign nations, FHWA is obligated to initiate government-to-government cultural resource consultations on transportation projects for which federal funding is involved.  FHWA Colorado Division has delegated all consultation activities in this regard to CDOT.  The CDOT Staff Archaeologist is the individual charged with undertaking and/or coordinating all aspects of Native American consultation on a project-by-project basis.

Neither FHWA nor CDOT has implemented a formal written policy that addresses the broad range of issues that comprise cultural resources consultation with indigenous tribal groups.  However, until such time as an explicit and comprehensive policy is enacted, consultation will proceed as follows:

- Tribal consultation is required for every federal-aid transportation project in Colorado for which an Environmental Assessment (EA) or Environmental Impact Statement (EIS) is prepared.  Projects involving unique or controversial issues of potential significance to Native Americans may also involve consultation, at the discretion of the Staff Archaeologist.

- The Staff Archaeologist will initiate and complete the consultation process, or must approve in advance a consultant to conduct the work under his supervision.  In all cases, however, the Staff Archaeologist must be notified—and will coordinate—this work.

- Forty-five tribes located throughout the Plains, Southwest and greater Intermountain West have expressed an interest in cultural resources consultation in Colorado on a county-specific basis.  The Staff Archaeologist has developed a complete and updated list of tribes and tribal contacts, each of which is cross-referenced by county.

- The RPEM should notify the Staff Archaeologist early in the EA/EIS planning process in order for consultation to be properly coordinated.  Information regarding the proposed undertaking (i.e., a statement of purpose and need or project overview) must be forwarded to the Archaeologist so that this data can be transmitted to the Native American community in a succinct yet cogent manner.

- In most cases consultation is initiated by sending a registered letter to the tribal chairman and/or other designated representative outlining the proposed undertaking and requesting government-to-government consultation, at the discretion of the tribe.

- Two to three weeks after the letter has been sent, a follow-up telephone call is made to each tribe to ensure receipt of the correspondence, to solicit input, and to answer questions, as appropriate.  Repeated phone calls, faxes or Emails may be necessary in order to guarantee that the information has reached the correct individual or office.  However, if contact with a responsible tribal member has not been established after four phone calls (or other means) following the initial letter, a sufficient effort is presumed to have been made and no further actions are necessary.

It is important to note that Indian tribal governments—as sovereign nations—are not bound by many of the rules and regulations established for standard interagency coordination.  For example, whereas agencies such as SHPO must ordinarily respond to written, policy level correspondence within 30 days, tribes are under no such time constraints.  Consequently, time frames for consultation may vary widely, and, according to federal statute, tribes may enter the consultation process at any time.  However, both FHWA and CDOT prefer to initiate contact early in the planning stages of a project in order to encourage tribes to enter the consultation process in a timely fashion.

- CDOT is obligated to acknowledge and address any comments, questions or concerns voiced by tribes regarding an undertaking.  It may be necessary to coordinate one or more meetings to a project area involving interested tribal members during the consultation period; all travel costs, lodging, per diem and/or consultation fees incurred by tribes as a result of these meetings are the responsibility of the agency, as outlined in Executive Order 13175, Consultation and Coordination With Indian Tribal Governments.  Vehicle mileage, lodging and per diem costs are established by CDOT based on existing rates that vary depending on location, and therefore these costs may fluctuate from one project to the next.  The daily consultation fee (or “honorarium”) is a fixed price based on comparable agency rates for the Section 106 process.  CDOT has developed and implemented a compensation policy to guide the payment of fees and expenses in the context of the consultation process.

- The consultation process must be carefully documented by the Staff Archaeologist and/or his designated representative(s).  Depending on the complexity of the undertaking and other factors, a report outlining the consultation process and its results may be required.

- At the conclusion of consultation, all appropriate individuals associated with the undertaking will be notified by the Archaeologist, including, but not limited to, the RPEM and the FHWA Colorado Division Environmental liaison.

Detailed information regarding Native American consultation must be present in the EA or EIS, but must not contain information considered sensitive or privileged by a tribe.  A separate subheading for consultation under the Cultural Resources section is generally the most appropriate location for this information.