REVISION OF SECTION 614

MICRO LOOP DETECTOR INSTALLATION

Section 614 of the Standard Specifications is hereby revised for this project as follows:

Subsection 614.10, (g) is deleted and replaced with the following:

(g)	A 9.375 mm wide by 75 mm deep (3/8" wide by 3" deep) saw cut shall be made between the micro loop in the lane and the pull box special located on the lane line as shown on the plans.  The saw cut shall be cleaned with water and dried with compressed air.

Micro loops shall be placed in 25 mm (1") diameter holes drilled to a depth of 0.6 meter (24") into the roadway at locations shown on the plans. The width will allow for a small clearance to maintain a vertical position, regardless of the slope or the grade of the roadway. The depth will allow for approximately 75 mm (3") of debris to settle to the bottom of the hole during drilling and eliminate the need for cleaning.

The micro loop shall be placed vertically in the hole and the micro loop cable placed in the saw cut back to the pull box special. Clean, dry, fine sand shall be placed in the hole around the micro loop. The micro loop shall be slowly lifted to a point of not less than 0.45 meters (18") from the top of roadway surface to the bottom of the micro loop to provide maximum detection. The hole then shall be fully filled with sand to a point that is level with the bottom of the saw cut.

Micro loop cables for through lanes and left turn lanes shall be run separately to the pull box special. Each cable shall be spliced in the pull box special to individual lead in cables back to the controller.

After the micro loops and cables are installed, the saw cuts and micro loop holes shall be filled with an approved two part, self curing, self bonding weatherproof epoxy or an approved alternative material.