REVISION OF SECTION 630

GLARE SCREEN (TEMPORARY)

Section 630 of the Standard Specifications is hereby revised for this project as follows:

Subsection 630.01 shall include the following:

This work shall consist of furnishing, installing, and maintaining glare screen of the size and type shown on the plans at the locations shown on the plans and in accordance with these specifications.  Glare screen installed on this project shall remain the property of the Contractor.

Subsection 630.09 shall include the following:

Glare screen shall be one that is included on the Department’s Approved Products List.  Blade height shall be a minimum of 24 inches.

Subsection 630.13 shall include the following:

Glare screen shall be installed according to the manufacturer's suggested method of installation.  The Contractor shall submit to the Engineer for approval, drawings showing the type of glare screen to be used and the method of installation to be implemented.

Subsection 630.15 shall include the following:

Glare screen will be measured by the linear foot.

Subsection 630.16 shall include the following:

The accepted quantity of glare screen will be paid for at the contract unit price per linear foot, which price shall be full compensation for all material, labor, tools, and equipment necessary to complete the work.

Payment will be made under:

Pay Item						Pay Unit

Glare Screen (Temporary)				Linear Foot